ITU    CIVIL ENGINEERING FACULTY

WATER SUPPLY AND ENVIRONMENTAL SANITATION

###### RECITATION 2 —

###### FLOW CHARACTERISTICS

1st Question:

It is considered that there is 20% leakage loss in the water supply network of a town. Total discharge pumped to the network is 1000 lt/s. If the pressure head of the network is decreased to 25 m from 50 m, what will be the amount of saved fresh water discharge?

2nd Question:

Maximum hourly fresh water consumption (max. qhr) of a county composed of 10 blocks each containing 30 condos is  450 l/individual/day. Consider a mean population of 5 people per condo.

a) Find the water demand of this county on hourly and daily basis ( =  = 1.5).

b) If the water demand of the county is pumped by means of pumps, what is the total amount of water that will be pumped to the system for a 30 years of operation time.

3rd Question:

A river having a drainage area of 453 km2 has a minimum discharge of 0.984 l/s/km2.

(Consider max. qday = 430 l/ind./day)

a) How many people’s water demand can be supplied from the river?

b) If a dam with 14 000 000 m3/year capacity is constructed on the river, how many people’s water demand can be supplied from the river?

4th Question:

Population of Side was 200 000 at 1980, and since this year an arithmetical increase is considered for the future population estimates (= 1.4, mean qday = 100 l/ind./day, ka = 3000).

- If a waste water disposal utility with a capacity of 35 000 m3/day was present at 1980, calculate until when this utility can be used without any modification.

- Calculate to what amount should the water consumption be reduced to use this utility until the year 2000 without any modification.