ITU    CIVIL ENGINEERING FACULTY

WATER SUPPLY AND ENVIRONMENTAL SANITATION

###### RECITATION 4 —

###### WATER TRANSMISSION LINES

1st Question:

A pumping station working 12 hours a day is pumping water to a distribution reservoir through a transmission line of length 2500 m in order to supply the water demand of a population of 21600. The water level of supply reservoir is 25 m and distribution reservoir is 100 m. Neglecting the local head losses, calculate the required power of pump (mean qday = 150 l/ind./day,  = 1.5, f =0.03,  = 0.65, also D = De).

2nd Question:

The transmission line (seen in the figure) having 40 cm pipe diameter is used to transmit water from supply reservoir A to distribution reservoir D. It is originally planned for 30 000 people, but its capacity is reached and a new planning is necessary for 50 000. If it is not possible to reconstruct the transmission line, find the power and location of a pumping station which is to be made on the transmission line (max qday = 200 l/ind./day, f = 0.03,  = 0.65).

# Text boxes

D

977.00

1000.00

8000 m                                                                       2000 m

B

A

940.00