12366 dnk201e dynamics - sample problems   2

Problem 1: An 90000-kg airplane lands at a horizontal speed of 65 m/s and a vertical descent of 2.5 m/s. The height  h of the rebound after the second bounce on the runway is 1.25·10-3 m. Assuming that there is no friction, aerodynamic lift, or engine thrust involved, and treating the airplane as a particle,

- calculate the coefficient of restitution e.

- Find the height h1 of the rebound after the first bounce.

- Calculate the impulse at the first bounce.

- Calculate the impulse at the second bounce.

- Find the percentage n of energy, that has been lost after the second bounce.

Problem 2: A Ferris wheel has three evenly spaced cages which weigh 500 kg with riders. For the position shown,  and .

- Calculate the total kinetic energy of the cages.

- Calculate the total angular momentum of the cages.

Now consider that moments and  are applied to this system for a time of 0.03 s.

- Determine the new   and , assuming that the system is still in the same position shown.

Problem 3: The disc in the figure below is rotating clockwise at an angular speed . Find the angular velocity and angular acceleration of the arms AB and BC.

# Text boxes

m=90000 kg

2.5 m/s

65 m/s

r = 6 m