## Chapter 10 - Moments of Inertia of Areas

Consider the beam shown below

Internal forces are distributed forces whose magnitudes vary linearly with the distance y from an axis passing through the centroid of the section.

Total resultant:

1st moment, Qx

The moment:

2nd moment, Qxx

Moment of inertia

## Moment of inertia of an area by integration

dA = (a - x)dy				dA = ydx

Rectangular moments of inertia

Polar moment of inertia

## Radius of gyration of an area

Has moment of inertia

Concentrate this area in a thin strip

If a strip is to have same moment of inertia,

the strip should be placed as shown.

By def:

Thus:

or

Radius of gyration - the distance, from an axis which passes through the CG, at which all the area or mass of an object could be concentrated without changing its moment of inertia.

## Parallel- Axis Theorem

Consider:

Moment of inertia with respect to AA'

MOI, I  W.R.T. 	1ST moment		total area

Centroidal Axis	W.R.T. BB.

Centroid, C, is

located on BB'

Parallel axis theorem

The moment of inertia of an area W.R.T. to any given axis AA' is equal to the MOI  of the area with respect to the centroidal axis plus .  Product of area, A, and the square of the distance d between the 2 axes.

The parallel axis theorem can be applied only if one of the two parallel axes passes through the centroid of the area.

Example

1). Given:

Find: Moment of inertia of shaded area with respect to the y-axis.

dA = ydx