## Slide 1: GEODETIC NETWORK DESIGN
Assoc. Prof. Dr. Rahmi Nurhan ÇELİK
ITU Department of
Geodesy & Photogrammetry
Division of Geodesy
Tel: 0212-2853822
e-mail: celikn@itu.edu.tr
http://www.celikrn.info
http://atlas.cc.itu.edu.tr/~celikn
http://www.geoitu.org

## Slide 2: Table of Contents
Introduction
What is the Mission of Geodesy?
Control Survey
Definitions
Datum
  Geodetic Datum
  Horizontal Control Datum
  Vertical Control Datum
  Turkish National Datum
Classification of Geodetic Network
National Geodetic Networks

## Slide 3: References
Açıklamalı Örneklemeli Büyük Ölçekli Haritaların Yapım Yönetmeliği, Harita ve Kadastro Mühendisleri Odası İstanbul Şubesi Yayını, 1989
Büyük Ölçekli Harita ve Harita Bilgileri Üretim Yönetmeliği, 15 Temmuz 2005 Günlü 2005-9070 Sayılı Resmi Gazete
1/5000 Ölçekli Standart, Topografik, Fotogrametrik Harita Yapımına ait Teknik Yönetmelik, 17 Ocak 1976 Günlü 15471 Sayılı Resmi Gazete
Ölçme Bilgisi, Celal Songu Matbaa Teknisyenleri Basımevi, İstanbul 1970

## Slide 4
Ölçme Bilgisi (Pratik Jeodezi), Erdoğan Özbenli-Türkay Tüdeş, Matbaa Teknisyenleri Basımevi, İstanbul 1972
Topografya (Ölçme Bilgisi) M. Gündoğdu Özgen, Teknik Üniversite Matbaası, İstanbul 1982
Güncel Gelişmeler Işığında Mekansal Bilgi Sistemleri İçin Jeodezik Altyapı ve Problemler, A. Aksoy, T. Ayan, R. N. Çelik, H. Demirel, R. Deniz, O. Gürkan, TMMOB Harita ve Kadastro Mühendisleri Odası İstanbul Şubesi Mesleki Tanıtım Yayın Komisyonu, Eğitim Dizisi 2, 28 Mayıs 1999.

## Slide 5
Geodesy, G. Bomford, Third Edition,Oxford University Press Amen House, London E.C.4, 1952
Elementary Surveying, P.r. Wolf-R.C.Brinker,Eight Edition, HarperCollinsPublishers Inc.,1989
Vermessung Kunde II, W. Grossmann-H. Kahmen, Sammhing Göschen de Gruyder, Berlin-NweYork 1988
Handbuck der Vermessungskunde, Band II, Jordan-Eggert-Kneiss, J.B. Metzlersche Verlagsbuchhandlung; Stuttgart 1963

## Slide 6: Grading Policy
Grade
1 Quiz %20
1 Project %20
1 Seminar %20
1 Midterm %40
Term Total %50
1 Final Exam %50
Attendance %00 %70

## Slide 7: INTRODUCTION

## Slide 8: What is the mission of GEODESY?
The Mission of Geodesy is to define,
  the shape and the gravity field of the Earth
  and also the changes of these by time.

## Slide 9
Therefore, there are 3 main problems occur.
To define the surface geometry of the Earth which is topography
To define the mathematical shape of the Earth which is Geoid
To define the best-fit ellipsoid of the Earth which is the Reference Ellipsoid
Note: Defining Geoid and Ellipsoid is in the subjects of Physical Geodesy

## Slide 10: How to define topography?
Detail survey must be carried out
All characteristic points must be measured
Precise position information must be obtained for all detail points
Therefore, error propagation must be taken care of
Thus control survey must be carried out

## Slide 11: Control Survey
There are three general types of control surveys:
Horizontal Vertical Gravity
However Gravity network will not be studied in this lecture. Horizontal surveys over large areas generally establish geodetic latitudes and longitudes of stations. From these values plane rectangular coordinates, usually in a Transverse Mercator (TM) or Universal Transverse Mercator (UTM) coordinate system can be computed. On control surveys of smaller areas, plane rectangular coordinates may be determined directly without obtaining geodetic latitudes and longitudes.

## Slide 12
Control surveys establish precise horizontal and vertical positions of reference monuments. These serve as the basis for originating or checking subordinate surveys for projects such as topographic and hydrographic mapping; property boundary delineation; and route and construction planing, design, and layout. They are also essential as a reference frame work for giving locations of data entered in Land Information Systems (LIS) and Geographic Information Systems (GIS)

## Slide 13: DEFINATIONS

## Slide 14: Ground Control Stations Coordinates and heights of stations are known in National Geodetic System
Horizontal Control Stations:
First, second and third order stations of National Geodetic Network (NGN) and also third order densification stations of NGN, densification stations for detail measurements, and traverse stations
Densification Stations for Detail Measurements:
Third-order Class I, Class II, high-precision traverse stations, and photogrammetric stations.

## Slide 15: Ground Control Stations Coordinates and heights of stations are known in National Geodetic System
Vertical Control Stations:
These are variable order National Vertical Networks (NVN) stations and other levelling stations whose definition are given in the Production Regulation of Large Scale Map.
Traverse stations:
These are the stations whose coordinates are computed using control stations within a traverse computation. The main polygon line should be no longer than 1600 meters.

## Slide 16: Densification Areas
Third-order Densification Area:
This is the area that exceeds at least 5 km of cadastral regions for cadastral works, municipality boundary regions that also includes neighbouring area for technical municipality services and public improvements works, and map survey area for nationalisation and engineering projects.
Densification Area for Detail Survey:
Cadastral work and map survey areas within the third-order densification area.

## Slide 17: Class I Stations
These are the horizontal stations whose coordinates are obtained using higher-order stations within a station adjustment computation; and it can also provide coordinates to the other stations.
Moreover, one of the range of stations, whose coordinates are obtained using these or higher-order stations, might be longer than 3 km away from these stations.

## Slide 18: Class II Stations
These are the horizontal station that cannot provide coordinates to the other stations. Moreover, coordinate of Class II stations can only be computed using higher-order stations shorter than 3 km away from the stations

## Slide 19: High-precision Traverse Stations
These are the horizontal stations that are established between the horizontal stations that can provide coordinates to these stations.
Coordinates of these stations are computed using traverse computation.
The range between the traverse stations can be between 800 and 1500 meters; and total length of this polygon line must be shorter than 7 km; and number of stations within 7 km must be less than 7.

## Slide 20: Photogrammetric Control Station
These are the control stations whose coordinates are computed using photogrammetric control survey method.

## Slide 21: GEODETIC DATUM
A set of constants specifying the coordinate system used for geodetic control, i.e., for calculating coordinates of points on the Earth.
At least 8 constants are needed to form a complete Datum:
3 for specifying the location of the origin of the coordinate system.
3 for specifying the orientation of the coordinate system.
2 for specifying the dimension of the reference ellipsoid.

## Slide 22: Horizontal Control Datum
A geodetic datum specifying the coordinate system in which horizontal control points are located
Horizontal Datum Parameters:
2 parameters for locating the control network
1 parameter for orienting the control network
1 parameter for scaling the control network

## Slide 23: Vertical Control Datum
A set of fundamental elevations to which other elevations are referred.
Sea Level Datum
An equipotential surface passing through a specified point at mean sea level which is used as a reference for elevations.
A surface passing through mean sea level at certain specified points to which elevations determined by levelling are referred.

## Slide 24: Turkish National Geodetic Datum
European Datum 1950
ED50
Reference Ellipsoid:
International Hayford 1910
Semi-major axis : 6,378,388. m
1/Flattening : 297

## Slide 25: Have a nice week to you all...

## Slide 26: National Network in Turkey

## Slide 27
Geoid: the equipotential surface of the Earth’s gravity field which best fits, in the least squares sense, mean sea level. In practice, the average position of sea level and a corresponding average over the time-varying geopontential must be accepted.

## Slide 31
Flattening (f)
Semi-major axis (a)

## Slide 32
Mean Sea Level

## Slide 34: A

## Slide 43: B

## Slide 52: C

## Slide 53: Horizontal Datum Parameters

## Slide 59: OR