## Slide 1: GEODETIC NETWORK DESIGN
Assoc. Prof. Dr. Rahmi Nurhan ÇELİK
ITU Department of
Geodesy & Photogrammetry
Division of Geodesy
Tel: 0212-2853822
e-mail: celikn@itu.edu.tr
http://www.celikrn.info
http://atlas.cc.itu.edu.tr/~celikn
http://www.geoitu.org

## Slide 2: Table of Contents
Introduction
What is the Mission of Geodesy?
Control Survey
Definitions
Datum
  Geodetic Datum
  Horizontal Control Datum
  Vertical Control Datum
  Turkish National Datum
Classification of Geodetic Network
National Geodetic Networks
Reconnaissance Sketch
Progress Sketch
Numbering Control Stations
Station Buildings
Station Description Sketch
Effects on Geodetic Network Design

## Slide 3: Classifications of Geodetic Networks
Specific Geodetic Networks
Regarding Measurement Methods
Regarding Geometry

## Slide 4: National Geodetic Network

## Slide 5
When a country or a group of countries land surveying is considered the control network which will be established is called National Geodetic Network. It is generally formed producing national maps. However it is also used defining the geometry of the Earth in the international corporation, and is also used within the scientific researches, like obtaining the mean ellipsoid, best-fit ellipsoid or reference ellipsoid

## Slide 6
There are generally two ways of establishing National Geodetic Network
a) Surface of the country is covered with large triangles (lengths of the triangles are about 15-20 km). In other words a large triangulation is established. Thereafter it is densificated with smaller triangles, lengths are about 5 to 10 km. Firstly the large triangulation is adjusted and the control stations of this network are called first -order stations. Secondly the smaller triangulation is computed and its stations are called as second-order stations. Then much smaller triangles are established (1 to 3 km) to densificate the second-order stations and these stations are called as third-order stations.

## Slide 7
However this kind of networks is usually established in small countries, i.e. Finland, Holland, Germany etc.
b) The other way of setting up National Geodetic Network is to cover all over the country with rings of chain networks rather than triangles. This method is also used in our country. It was generally used in USA, Russia, India, Spain etc., since this method is suitable to cover the countries whose lands are very large.
This method allows us to start establishing National Geodetic Network from the prior areas without loosing the integrity of the whole network.

## Slide 8
In our country rings of chains had been formed from West to East and North to South. The shape of these rings are close to squares and rectangles of about 200 to 250 by 200 to 250 km, and there are totally 27 rings of chain network.
A base had been measured at each corner of the rings. Total number of measured bases is 41. Laplace stations (Latitude, Longitude, and Azimuth: astronomic observation) had been set almost at each corner and in the middle of some rings. These stations are called as astronomic stations. The National Geodetic Network had been located and oriented based on those stations. Stations in the chains are called first-order stations and lengths between the stations are 25 to 35 km.

## Slide 9
The large rings of chains are divided into smaller rings with the shorter chain of triangles. The stations in these chains are called second-order stations and the lengths between these stations are 20 to 30 km.
Coordinates of first and second order stations are computed using geographic and projection coordinates within the adjustment computation.
Within the first-order chain rings and the space left from the second order chains are filled with the stations whose coordinates are computed in station adjustment and the length between stations are about 10 km. These are also called second-order stations.

## Slide 10
Then these are densificated with the stations whose lengths are about 4 to 15 km using the combination of intersection and resection methods. These new stations are called third-order stations. Thereafter these are densificated using Class I, Class II and high precise traverse stations.
All of these geodetic stations constitute the National Geodetic Network (NGN)
Foundation of NGN was began in 1942
99 Astronomic Stations
904 + 3320 First + Second order stations
27 Rings of Chains
8 Stations have been taken from the West part to integrate the system to ED50. Adjustment process of NGN were carried out in 1954.

## Slide 11: Geodetic Network Design
Reconnaissance Sketch
Progress Sketch
Numbering Control Stations
Station Buildings
Station Description Sketch

## Slide 12: Reconnaissance Sketch
Using the small scale map, all first, second and third order control stations within the densification area are obtained and a reconnaissance sketch is drawn. The number of stations obtained within the area should be higher than 3 and they should be well distributed.
On the reconnaissance sketch, boundary of densification area, boundary of urban area, status of transportations, forest and grovel areas, rivers, streams, lakes and all similar objects are shown.
Scale of the sketch is arranged with respect to the size of the area work with.

## Slide 13: Progress Sketch
A map or sketch showing the current state of survey.
In triangulation and traversing, each point established, lines observed over, and base lines measured are shown on the progress sketch.
In levelling, the progress sketch shows the route followed and the towns passed through but not necessarily the location of the bench marks.

## Slide 14: Numbering Control Stations
According to the regulation, all stations established are numbered regarding the base of 1/100,000 scale map area.
In UTM System, 4 zones are exist for Turkey and their mid longitude are 27o, 33o, 39o and 45o.
1/100,000 scale map index letters from North to South are D, E, F, G, H, I, J, K, L, M, N, O, P, R, S, T, U and the numbers from West to East are 15, 16, 17, ….. 51, 52, 53.
For instance a name of 1/100,000 scale map can be F16, K22, M28.

## Slide 15: Numbering Control Stations
A number of a control station constitutes 7 digits.
First 3 digits are used to define the name of the 1/100,000 scale map.
The other 4 digits left show the number of control stations. The numbers are dedicated to the control stations with respect to the type of the stations.
Third order stations are numbered starting from 0001 to 0500 i. e. G250164, F160001, M280476.

## Slide 16: Numbering Control Stations
The other control stations are numbered starting from 0501 to … i. e. F160507, M289987
photogrammetric control stations are also numbered as the other control stations.
Numbers of the stations are given with respect to the calculation order.
First, second and third order control stations used to obtain the coordinates of new stations are renumbered and their old numbers are shown as sub-name of the new one i. e. F160001/4200, K220026/4005

## Slide 17: Station Buildings
All new control stations that are planned to be established are built on the ground in the working area. The type and size of monuments for the stations are described in the regulation book with their plan view.
These monuments are not suitably built only to set an instrument on, they are also built to be easily seen and observed from the other stations.

## Slide 18: Station Description Sketch
These sketches are drawn to reach the field where control stations were build, and then find the exact location of monument of the stations on the ground.
Therefore, these sketch should clearly be drawn and also should contain detail description information about reaching the point.

## Slide 19: Effects on Geodetic Network Design
Precision Measures
  Positional Precision Measures
  Error Ellipse
Local Precision Measures
  Relative Error Ellipse
Reliability
Economy

## Slide 20: 1:100000 Key Chart

## Slide 21: Have a nice week to you all...

## Slide 22: 1:100000 Key Chart

## Slide 23: National Network in Turkey

## Slide 24: Classifications Regarding Geometry
Central Networks
  Pentagon
  Hexagon
Chain Networks
Quadrilateral Networks
Semi-Central Networks
Complex Networks

## Slide 25: Classifications Regarding Measurement Methods
Triangulation
Trilateration
Combined

## Slide 26: Specific Geodetic Networks
These control networks are specifically designed for precise engineering projects. Using these networks, precise detail surveys are carried out to produce the maps of the area. Then, stake out survey are precisely carried out based on these networks.
These networks are named regarding the project, like
Anadolu Highway Geodetic Network
Haliç Bridge Geodetic Network.

## Slide 27: Central Network

## Slide 28: Semi-central Network

## Slide 29: Quadrilateral Network

## Slide 30: Chain Network

## Slide 31: Complex Network

## Slide 32: Triangulation

## Slide 33: Trilateration

## Slide 34: Combined

## Slide 35
Flattening (f)
Semi-major axis (a)

## Slide 36
Mean Sea Level

## Slide 38: A

## Slide 47: B

## Slide 56: C

## Slide 57: Horizontal Datum Parameters

## Slide 63: OR