## Slide 1: GEODETIC NETWORK DESIGN
Assoc. Prof. Dr. Rahmi Nurhan ÇELİK
ITU Department of
Geodesy & Photogrammetry
Division of Geodesy
Tel: 0212-2853822
e-mail: celikn@itu.edu.tr
http://www.celikrn.info
http://atlas.cc.itu.edu.tr/~celikn
http://www.geoitu.org

## Slide 2: Table of Contents
Introduction
What is the Mission of Geodesy?
Control Survey
Definitions
Datum
  Geodetic Datum
  Horizontal Control Datum
  Vertical Control Datum
  Turkish National Datum
Classification of Geodetic Network
National Geodetic Networks
Reconnaissance Sketch
Progress Sketch
Numbering Control Stations
Station Buildings
Station Description Sketch
Effects on Geodetic Network Design

## Slide 3: Table of Contents
Direction Observation
Adjustment of Observations At A Station
Axis of Theodolites
Errors of Theodolites
Natural Errors
Personal Errors
Common Mistakes

## Slide 4: Direction Observation

## Slide 5: Adjustment of Directions At A Station

## Slide 6
N
0
2
3
1
4
z
x1
x2
x3
z0

## Slide 7: Observation Equation
v1’ = -l1’ + z’
v2’ = -l2’ + z’ + x1
v3’ = -l3’ + z’ + x2
v4’ = -l4’ + z’ + x3
[v’] = -[l’] + 4z’ + x1 +x2 + x3 = 0
v1’’ = -l1’’ + z’’
v2’’ = -l2’’ + z’’ + x1
v3’’ = -l3’’ + z’’ + x2
v4’’ = -l4’’ + z’’ + x3
[v’’] = -[l’’] + 4z’’ + x1 +x2 + x3 = 0
I. Obs. Set
II. Obs. Set

## Slide 8
v1’’’ = -l1’’’ + z’’’
v2’’’ = -l2’’’ + z’’’ + x1
v3’’’ = -l3’’’ + z’’’ + x2
v4’’’ = -l4’’’ + z’’’ + x3
[v’’’] = -[l’’’] + 4z’’’ + x1 +x2 + x3 = 0
4z’ + x1 + x2 + x3 -[l’] = 0
4z’’ + x1 + x2 + x3 -[l’’] = 0
4z’’’ + x1 + x2 + x3 -[l’’’] = 0
4[z] + 3x1 + 3 x2 + 3x3 -[l] = 0
III. Obs. Set
z’ + z’’ + z’’’ = [z]

## Slide 9
v1’ + v1’’ + v1’’’ = [v1] = -l1’ - l1’’ - l1’’’ +z’ + z’’ + z’’’
[v1] = -[ l1] + [z]
[v1] = 0
[z] = [ l1]
v2’ + v2’’ + v2’’’ = [v2] = - [ l2] + [z] + 3x1
[v2] = 0 = - [ l2] + [ l1] + 3x1
x1 = ([ l2] - [ l1] ) / 3

## Slide 10
v3’ + v3’’ + v3’’’ = [v3] = - [ l3] + [z] + 3x2
[v3] = 0 = - [ l3] + [ l1] + 3x2
x2 = ([ l3] - [ l1] ) / 3
v4’ + v4’’ + v4’’’ = [v4] = - [ l4] + [z] + 3x3
[v4] = 0 = - [ l4] + [ l1] + 3x3
x3 = ([ l4] - [ l1] ) / 3

## Slide 11
3 x1 [z] - [ l2] = 0
3 x2 [z] - [ l3] = 0
3 x3 [z] - [ l4] = 0
-3 x1 -3 x2 -3 x3 - 4[z] - [ l ] = 0
- [z] + [ l1] = 0
[ l1] = [z]
If normal equations of x are written together with the multiplication of
normal equation of z by -1

## Slide 12
When these equations are generalised,
Number of Obs. Set : n
Number of Directions : s
x1 = [ l2] /n - [ l1] /n z’ = ([ l’] - (x1 + x2 +…….xs-1))/s
x2 = [ l3] /n - [ l1] /n z’’ = ([ l’’] - (x1 + x2 +…….xs-1))/s
. . . . . .
. . . . . .
. . . . . .
xs-1 = [ ls] /n - [ l1] /n z(n)= ([ l(n)] - (x1 + x2 +…….xs-1))/s
Above equations show that, in order to obtain adjusted directions,
mean of first directions is subtracted from the mean of the other directions.

## Slide 13
l1’ = l1’’ = l1’’’ = 0
v1’ = z’ , v1’’ = z’’ , v1’’’ = z’’’
[z] = v1’ + v1’’ + v1’’’ = 0
v1’ = (0 - l1’) + z’ = d1’ + z’
v2’ = (x1 - l2’) + z’ = d2’ + z’
v3’ = (x2 - l3’) + z’ = d3’ + z’
v4’ = (x3 - l4’) + z’ = d4’ + z’
[v’] = [x - l’] + 4z’ = [d’] + 4z’
[v’] = 0  z’ = [d’] /4
v1’ = d1’ - [d’] /4
Therefore first directions are reduced to zero, as a result of this,
In order to obtain root mean square (rms) of the adjusted directions

## Slide 14
v1’ = d1’ - [d’] /4
When above equation is generalised,
vi’ = di’ - [d’] /s
is obtained.
l1’ = l1’’ = l1’’’ = 0
d1’ = d1’’ = d1’’’ = 0
This result shows a practical rule to obtain residuals (v).
Having reduced the observation sets to zero. Mean of observation
sets is calculated to obtain the adjusted value of directions.
(x-l) gives d values. The mean of d values gives the z values
for each set of observation. If these are subtracted from d
residuals are obtained.

## Slide 15
In order to obtain [vv]
[vv] = [v’v’] + [v’’v’’] + [v’’’v’’’]
vi’.vi’ = di’ . di’ - 2 di’ [d’]/s + [d’] .[d’] / s2
[v’.v’] = [d’ . d’] - 2 [d’][d’]/s + s.[d’] .[d’] / s2
[v’v’] = [d’ d’] - [d’]2
[v’’v’’] = [d’’ d’’] - [d’’]2
[v’’’v’’’] = [d’’’ d’’’] - [d’’’]2
[vv] = [dd] - 1/s [d]2

## Slide 16
Number of observation : n.s
Number of unknown : s - 1 , n (directional unknowns)
m =  [v v] / r
r = n . s - (s - 1+ n) = s (n - 1) - (n - 1) = (n - 1) (s - 1)
m=  [v v] / (n-1) (s-1) =  [dd] -1/s [d]2
rms of mean of observation sets
mort = m /  n
rms of an angle measurements
m = m /  2
rms of an angle obtained from mean of observation set
(m)ort = mort /  2

## Slide 17: Axis of Theodolites

## Slide 18: Errors of Theodolites
Plate bubbles out of adjustment.
If the axes of the plate bubbles are not perpendicular to the vertical axis, the latter will not be truly vertical when the plate bubbles are centered. This condition causes errors in measured horizontal and vertical angles that cannot be eliminated by averaging direct and reversed readings. Plate bubbles are out of adjustment, if, after centering, they run when the instrument is rotated 200g in azimuth. The length of bubble run shows double the vertical axis tilt, which is then made truly vertical by bringing the bubbles back halfway using the foot screws. When plate bubbles are maladjusted, angles can be measured but it is inconvenient and time consuming, so the required adjustment should be made.

## Slide 19
Axis of sight not perpendicular to the horizontal axis.
If this condition exists, as the telescope is plunged, the axis of sight generates a cone whose axis coincides with the horizontal axis of the instrument. The greatest error from this source occurs when plunging the telescope, as in prolonging a straight line or measuring deflection angles. Also, when the angle of inclination of the backsight is not equal to that of the foresight, measured horizontal angles will be incorrect. These errors are eliminated by double centering and by averaging equal numbers of direct and reversed readings.
Horizontal axis not perpendicular to the vertical axis.
This situation causes the axis of sight to define an inclined plane as the telescope is plunged and, therefore, if the backsight and foresight have differing angles of inclination, incorrect horizontal angles will result. Errors from this origin can also be cancelled by averaging an equal number of direct and reversed readings.

## Slide 20
Axis of the telescope bubble not parallel to the axis of sight
If this occurs for a transit, the axis of sight is inclined upward or downward when the telescope bubble is centered. It causes an error in vertical angles. The effect is eliminated in vertical angles by averaging equal numbers of direct and reversed readings or applying an index error correction.
Eccentricity of centers
Errors from this source are minimised by taking readings at several positions on the circle so they are spaced around the entire arc, and the results averaged. 200 / n
Unsteady tripod
Tripod leg bolts must be tight so there is neither play nor strain (they can be tapped lightly to relieve any stress before taking the first sight), and the shoes set solidly in the ground. To eliminate strain, some surveyors loosen wing nuts and re-tighten after planting the legs and before leveling the instrument.

## Slide 21
Wind
Wind vibrates a transit and deflects the plumb bob. Shielding the instrument, or even suspending observations on precise work, may be necessary on windy days. An optical plummet is helpful in this situation.
Temperature effects.
Temperature differentials cause unequal expansion of various parts of theodolites. A level bubble is drawn toward the heated end of the vial, as can be checked by blowing on one end of the vial and noting movement of the bubble, then re-levelling and checking the position of the cross hairs on a target. Temperature effects are reduced by shielding instruments from sources of heat or cold.
Natural Errors

## Slide 22
Refraction
Unequal refraction bends the line of sight and may cause an apparent shimmering of the observed object. It is desirable to keep lines of sight well above the ground and avoid sights close to buildings, smokestacks, and even large individual bushes in generally open spaces. In some cases, observations may have to be postponed until atmospheric conditions have improved.
Settling of the tripod
The weight of an instrument may cause the tripod to settle, particularly when set up on soft ground or blacktop pavement. When a job involves crossing swampy terrain, stakes should be driven to support the tripod legs and work at a given station completed as quickly as possible. Stepping near a tripod leg, or touching one while looking through the telescope, will demonstrate the effect of settlement on the position of the bubble and cross hairs.

## Slide 23
Instrument not set up exactly over the point
The plumb bob or optical plummet position should be checked at intervals during the time a station is occupied, to be certain it remains centered and the instrument is over the point.
Level bubbles not centered perfectly
The bubbles must be checked frequently, but NEVER releveled between a backsight and foresight-only before starting, and after finishing, an angle measurement. For horizontal angles, the telescope can be elevated or depressed in the vertical plane without affecting measurements if the standards are properly adjusted; hence, the bubble at right angles to the telescope is the important one.
Personal Errors

## Slide 24
Improper use of clamps and tangent screws
An observer must form good operational habits and be able to identify the various clamps and tangent screws by their touch without looking at them. Final setting of tangent screws is always made with a positive motion to avoid backlash. Clamps should be tightened just once and not checked again to be certain they are secure.
Poor focusing
Correct focusing of the eyepiece on the cross hairs, and of the objective lens on the target, is necessary to prevent parallax. Objects sighted should be placed as near the center of the field of view as possible. Focusing affects pointing, which is an important source of error.
Overly careful sights
Checking and double checking the position of the cross-hair setting on a target wastes time and actually produces poorer results than one fast observation. The cross hair should be aligned quickly and the next operation begun promptly.

## Slide 25
Sighting on, or setting up over, the wrong point
Calling out or recording an incorrect value
Reading the wrong circle
Turning the wrong tangent screw
Using haphazard field procedures
Common Mistakes

## Slide 26: Have a nice week to you all...