## Slide 1: GPS Technique
Assoc. Prof. Dr. Rahmi Nurhan ÇELİK
ITU Department of
Geodesy & Photogrammetry
Division of Geodesy
Tel: 0212-2853822
celikn@itu.edu.tr
http://atlas.cc.itu.edu.tr/~celikn

## Slide 2: Table of Contents
Space Techniques
What is GPS?
History of GPS.
How GPS works?
GPS Segments
  Space Segments
  Control Segments
  User segments
Positioning with GPS
  Measures of Accuracy
  Single Point Positioning
  Differential GPS
  Static GPS
    Static
    Rapid Static
  Kinematic GPS
  Real Time GPS

## Slide 3: Table of Contents
GPS Error Sources
GPS Observables
Coordinate Systems, Datum
Coordinate Transformations
GPS Project Management
GPS Data & Data Processing
GPS Receivers
GPS Applications
GPS in Turkey

## Slide 4: References
GPS Theory and Practice, , B. Hofmann-Wellenhof, H. Lichtenegger and J. Collins, Springer-Verlag, 4th edition, 1997. (2000 on sale)
Global Positioning System : Theory and Applications, Volume I & Volume 2. ., Edited by Bradford W. Parkinson & James J. Spilker, American Institute of Aeronautics and Astronautics, Inc., 1996.
GPS for Geodesy by P.J.G. Teunissen and A. Kleusberg, 2nd edition, Springer, 1998.
Linear Algebra, Geodesy, and GPS by Gilbert Strang & Kai Borre, Wellesley –Cambridge Press. 1997
Understanding GPS : Principles and Applications by Elliott D. Kaplan, Artech House Publishers., 1996.
GPS Positioning Guide, Caroline Erickson, Natural Resources Canada, Geodetic Survey Division Information services,July 1995, Third Printing

## Slide 5: Space Techniques
150 - 1,500 Remote sensing
1,500 - 20,000 Geodetic
>36,000 Communication
Hight above earth (km) Satellite types
There are several satellite techniques

## Slide 6: Space Techniques

## Slide 7: Satellite Laser Ranging SLR
Principle: Two way laser distance measurements are made from the ground stations to the artificial satellites carrying retro-reflectors

## Slide 8: SLR Ground Station

## Slide 9: Lunar Laser Ranging LLR
Principle: Two way laser distance measurements are made from the ground stations to the retro-reflectors placed on the shadow side of the lunar terminator.

## Slide 10: Very Long Baseline Interferometry VLBI
Principle: Radio signals broadcasted by Quasars, which are unusual astronomical objects, are received by the radio telescopes places on the ground.

## Slide 11: VLBI Ground Stations

## Slide 12: What is GPS ?

## Slide 13: What is GPS ?
Basics of GPS (3m 19s)
What is DGPS ? (3m 37s)
Advanced GPS (5m 6s)
GALILEO (6m 58s)

## Slide 14: History of GPS
The launch of the Sputnik satellite in 1957 was actually the beginning of GPS. Scientists studying the orbit of the satellite realised they could track the satellite by its radio signal. This in turn would mean that a person on earth could obtain his position on the globe if he could read the signal from the satellite in conjunction with knowing the exact orbit of the satellite.
In 1964, U.S. submarines began using this method for positioning known as the TRANSIT system of GPS. It required only one satellite but for that reason a reading could only be taken roughly every 35 - 45 minutes. The submarine also had to be sitting still.

## Slide 15: History of GPS
On May 31, 1967 the United States Navy launched the TIMATION I satellite which improved the TRANSIT system by embedding an atomic clock inside the satellite. The atomic clock could tell the user the length of time it took each signal to leave the satellite and reach the receiver. The user then knew the distance to the satellite. Most importantly, a navigation vehicle did not have to stop.
Although the TRANSIT system was a significant leap forward in GPS technology, it suffered from poor accuracy and was often inefficient. In the early 70's, the United States military began a program that would later be known as the NAVSTAR GPS program.

## Slide 16: History of GPS
Research and development for the Navstar system began in 1973. The system would offer several satellites for navigation as opposed to just one. Availability would be increased and mobile vehicles would not have to wait for long periods of time to get a reading. Originally named the Navigation Technology Program, the first four satellites of the Navstar constellation were launched in 1978.
Today, the Navstar system contains 24 satellites that circle the globe every 12 hours. 5 - 8 satellites are visible from any point on earth at any time although visibility should not be confused with availability. Satellites often sit too low to the horizon to be used effectively.

## Slide 17: How GPS Works?
The Global Positioning System
Measurements of code-phase arrival times from at least four satellites that are used to estimate four quantities: Position in three dimensions (X,Y,Z) and GPS time (T)
X,Y,Z,T
,,h,T

## Slide 18: How GPS Works?

## Slide 19: How GPS Works?

## Slide 20: Have a nice week !
Thank you ...