## Slide 1: GPS Technique
Assoc. Prof. Dr. Rahmi Nurhan ÇELİK
ITU Department of
Geodesy & Photogrammetry
Division of Geodesy
Tel: 0212-2853822
celikn@itu.edu.tr
http://atlas.cc.itu.edu.tr/~celikn

## Slide 2: Table of Contents
Space Techniques
What is GPS?
History of GPS.
How GPS works?
GPS Segments
  Space Segments
  Control Segments
  User segments
Positioning with GPS
  Measures of Accuracy
  Single Point Positioning
  Differential GPS
  Static GPS
    Static
    Rapid Static
  Kinematic GPS
  Real Time GPS

## Slide 3: Table of Contents
GPS Error Sources
GPS Observables
Coordinate Systems, Datum
Coordinate Transformations
GPS Project Management
GPS Data & Data Processing
GPS Receivers
GPS Applications
GPS in Turkey

## Slide 4: GPS Segments

## Slide 5: GPS Segments
Space Segment
Control Segment
User Segment

## Slide 6: Space Segment
The Space Segment of the system consists of the GPS satellites. These space vehicles (SVs) send radio signals from space.

## Slide 7: Space Segment
The nominal GPS Operational Constellation consists of 21+3 satellites that orbit the earth in 12 hours. There are often more than 24 operational satellites as new ones are launched to replace older satellites. The satellite orbits repeat almost the same ground track (as the earth turns beneath them) once each day. The orbit altitude is such that the satellites repeat the same track and configuration over any point approximately each 24 hours (4 minutes earlier each day). There are six orbital planes (with nominally four SVs in each), equally spaced (60 degrees apart), and inclined at about fifty-five degrees with respect to the equatorial plane. This constellation provides the user with between five and eight SVs visible from any point on the earth.

## Slide 8: Space Segment

## Slide 9: Space Segment

## Slide 10: Block-I Satellites
The Block I SVs, built by Rockwell International as developmental prototypes, were launched between 1978 and 1985 from VAFB, CA. These SVs supported most of the system testing. Out of a total of 11 Block 1 SVs launched on the Atlas-Centaur, one was lost as a result of a launch failure, three have reached end-of-life due to wear-out of their atomic clocks, and two suffered failures of their three-axis attitude control system. The oldest Block I SV (PRN #6) has operated reliably for more than double its five-year design life.

## Slide 11: Block-IIA Satellites
Block II SVs were built by Rockwell International. The first of 28 Block II SVs, SV PRN number 14, was launched on 14 February 1989 from Cape Canaveral AFS, FL using a Delta II MLV and was set "healthy" in its broadcast 50 Hz navigation message for global use on 15 April 1989. The last Block IIA was launched (TBD).
Significant Block II SV enhancements to the signal-in-space (SIS) interface were:
Radiation hardened electronics to prevent random memory upset events to improve SIS reliability and survivability.
Capacity to store 180 days worth of 50 Hz navigation message data, compared to only 3.5 days worth of storage in the Block I SVs, to guarantee SIS availability.
Full selective availability (SA) and anti-spoof (A-S) capabilities to provide for SIS security.
Automatic detection of certain error conditions and switching to non-standard PRN Code transmission or default navigation message data (alternating ones and zeros) to protect users from tracking a faulty SV and maximize SIS integrity.

## Slide 12: Block-IIR Satellites
During the middle of 1989, procurement began for 21 additional satellites ("replenishment SVs") from Lockheed Martin, formerly General Electric. The Block IIR SVs will present an identical SIS interface to the User Segment. Under a survivability scenario, the Block IIR SVs will have the capabilities to autonomously navigate (AUTONAV) themselves and generate their own 50 Hz navigation message data. These AUTONAV capabilities will enable the Block IIR SVs to maintain full SIS accuracy for at least 180 days without Control Segment support. AUTONAV will also significantly improve both the reliability and integrity of the broadcast SIS. Accuracy improvements are expected to be approximately 7 meters spherical error probable (SEP) in a full Block IIR constellation. Additional differences between IIR and IIA are:
…

## Slide 13: Block-IIR Satellites
NAVIGATION PAYLOAD
  additional radiation hardening
  cross link ranging
  reprogrammable micro-processor
  two atomic clocks on at all times (hot backup)
ELECTRICAL POWER SYSTEMS (EPS)
  3 Ni CAD to 2 NiH batteries
ATTITUDE AND VELOCITY CONTROL SYSTEMS (AVCS)
  manual acquisition/pointing to autonomous
SYSTEM DESIGN
  larger fuel capacity
  redundancy management system in SV processor
  The first launch of Block IIR SV is currently scheduled for 1996 on a launch on need (LON) basis.

## Slide 14: Block-IIR-M Satellites
Approximately eight of the latest Block IIR "replenishment" satellites will be modernized to include a new military code and a second civil signal called L2C. DID covered the Navstar GPS IIR-M program in a May 11/05 article. The two new signals on the IIR-M satellite will provide reduced vulnerability to interference and will allow for calculation of ionospheric corrections at the user's location. Additionally, service performance in accuracy, availability, integrity and reliability will be realized. The first IIR-M satellite is scheduled for launch later in 2005 . It was launched 25th September 2005

## Slide 15: Block-IIF Satellites
Further satellite modernization is also planned. The follow-on system for the Navstar GPS Block IIR-M will be the Block IIF "follow-on" satellite. These satellites will have the same capabilities as the Block IIR-M, plus a third civil signal called L5 to support civil aviation and other applications. Navstar GPS Block IIF will be the end of the current generation of GPS satellites.
The next-generation GPS system - Block IIIA - will introduce new capabilities to meet higher demands of military and civilian users. The system is looking ahead to its first launch in 2013.
Block IIIA will offer the opportunity for a cross-linked command and control architecture, allowing the entire GPS constellation to be updated from a single ground station instead of waiting for each satellite to orbit into view of a ground antenna. Block IIIA will also support a spot beam antenna that provides resistance to hostile jamming, improving its accuracy and integrity while reducing the vulnerability of GPS signals.

## Slide 16: Important Link for Space Segment UNITED STATES NAVAL OBSERVATORY
Current Constellation of GPS Satellites
  http://tycho.usno.navy.mil/gpscurr.html
Daily GPS constellation Status
  ftp://tycho.usno.navy.mil/pub/gps/gpstd.txt

## Slide 17: Control Segment
The Control Segment consists of a system of tracking stations located around the world.
The Master Control facility is located at Schriever Air Force Base (formerly Falcon AFB) in Colorado. These monitor stations measure signals from the SVs which are incorporated into orbital models for each satellites. The models compute precise orbital data (ephemeris) and SV clock corrections for each satellite. The Master Control station uploads ephemeris and clock data to the SVs. The SVs then send subsets of the orbital ephemeris data to GPS receivers over radio signals.

## Slide 18: Control Segment

## Slide 19: Control Segment

## Slide 20: User Segment
The GPS User Segment consists of the GPS receivers and the user community. GPS receivers convert SV signals into position, velocity, and time estimates. Four satellites are required to compute the four dimensions of X, Y, Z (position) and Time. GPS receivers are used for navigation, positioning, time dissemination, and other research.
Navigation in three dimensions is the primary function of GPS. Navigation receivers are made for aircraft, ships, ground vehicles, and for hand carrying by individuals.

## Slide 21: User Segment
Precise positioning is possible using GPS receivers at reference locations providing corrections and relative positioning data for remote receivers. Surveying, geodetic control, and plate tectonic studies are examples.
Time and frequency dissemination, based on the precise clocks on board the SVs and controlled by the monitor stations, is another use for GPS. Astronomical observatories, telecommunications facilities, and laboratory standards can be set to precise time signals or controlled to accurate frequencies by special purpose GPS receivers.
Research projects have used GPS signals to measure atmospheric parameters.

## Slide 22: User Segment

## Slide 23: GPS Segments
Control Segment
Space Segment
NAVSTAR : NAVigation
Satellite Time and Ranging
User Segment

## Slide 24: Positioning with GPS

## Slide 25: 3D+1D = 4D
h
X, Y, Z
Time


h
Z
X
Y
P
P

## Slide 26: Height
h
Topography
H
N
Elipsoid
Geoid
P

## Slide 27: Positioning with GPS
There are two
positioning services
Precise Positioning Service
Standard Positioning Service

## Slide 28: Precise Positioning Service (PPS)
Authorised users with cryptographic equipment and keys and specially equipped receivers use the Precise Positioning System. U. S. and Allied military, certain U. S. Government agencies, and selected civil users specifically approved by the U. S. Government, can use the PPS.
    PPS Predictable Accuracy
      22 meter Horizontal accuracy
      27.7 meter vertical accuracy
      200 nanosecond time (UTC) accuracy

## Slide 29: Standard Positioning Service (SPS)
Civil users world-wide use the SPS without charge or restrictions. Most receivers are capable of receiving and using the SPS signal. The SPS accuracy is intentionally degraded by the DOD by the use of Selective Availability.
SPS Predictable Accuracy
      100 meter horizontal accuracy
      156 meter vertical accuracy
      340 nanoseconds time accuracy
These GPS accuracy figures are from the 1999 Federal Radio-navigation Plan. The figures are 95% accuracies, and express the value of two standard deviations of radial error from the actual antenna position to an ensemble of position estimates made under specified satellite elevation angle (five degrees) and PDOP (less than six) conditions.

## Slide 30: Standard Positioning Service (SPS)
For horizontal accuracy figures 95% is the equivalent of 2drms (two-distance root-mean-squared), or twice the radial error standard deviation. For vertical and time errors 95% is the value of two-standard deviations of vertical error or time error.
Receiver manufacturers may use other accuracy measures. Root-mean-square (RMS) error is the value of one standard deviation (68%) of the error in one, two or three dimensions. Circular Error Probable (CEP) is the value of the radius of a circle, centred at the actual position that contains 50% of the position estimates. Spherical Error Probable (SEP) is the spherical equivalent of CEP, that is the radius of a sphere, centred at the actual position, that contains 50% of the three dimension position estimates. As opposed to 2drms, drms, or RMS figures, CEP and SEP are not affected by large blunder errors making them an overly optimistic accuracy measure

## Slide 31: Standard Positioning Service (SPS)
Receiver manufacturers may use other accuracy measures. Root-mean-square (RMS) error is the value of one standard deviation (68%) of the error in one, two or three dimensions. Circular Error Probable (CEP) is the value of the radius of a circle, centered at the actual position that contains 50% of the position estimates. Spherical Error Probable (SEP) is the spherical equivalent of CEP, that is the radius of a sphere, centered at the actual position, that contains 50% of the three dimension position estimates. As opposed to 2drms, drms, or RMS figures, CEP and SEP are not affected by large blunder errors making them an overly optimistic accuracy measure
Some receiver specification sheets list horizontal accuracy in RMS or CEP and without Selective Availability, making those receivers appear more accurate than those specified by more responsible vendors using more conservative error measures.

## Slide 32: GPS Satellite Signals

## Slide 33: GPS Satellite Signals
The SVs transmit two microwave carrier signals. The L1 frequency (1575.42 MHz) carries the navigation message and the SPS code signals. The L2 frequency (1227.60 MHz) is used to measure the ionospheric delay by PPS equipped receivers.
Three binary codes shift the L1 and/or L2 carrier phase.
The C/A Code (Coarse Acquisition) modulates the L1 carrier phase. The C/A code is a repeating 1 MHz Pseudo Random Noise (PRN) Code. This noise-like code modulates the L1 carrier signal, "spreading" the spectrum over a 1 MHz bandwidth. The C/A code repeats every 1023 bits (one millisecond). There is a different C/A code PRN for each SV. GPS satellites are often identified by their PRN number, the unique identifier for each pseudo-random-noise code. The C/A code that modulates the L1 carrier is the basis for the civil SPS.

## Slide 34: GPS Satellite Signals
The P-Code (Precise) modulates both the L1 and L2 carrier phases. The P-Code is a very long (seven days) 10 MHz PRN code. In the Anti-Spoofing (AS) mode of operation, the P-Code is encrypted into the Y-Code. The encrypted Y-Code requires a classified AS Module for each receiver channel and is for use only by authorized users with cryptographic keys. The P (Y)-Code is the basis for the PPS.
The Navigation Message also modulates the L1-C/A code signal. The Navigation Message is a 50 Hz signal consisting of data bits that describe the GPS satellite orbits, clock corrections, and other system parameters.

## Slide 35: GPS Satellite Signals

## Slide 36: GPS Satellite Signals
Fundamental Frequency 10.23 MHz
x 154
x 120
L1 1575.42 MHz
L2 1227.60 MHz
C/A Code 1.023 MHz
P-Code 10.23 MHz
P-Code 10.23 MHz
÷ 10
50 BPS
Satellite Message

## Slide 37: Measures of Accuracy

## Slide 38: Measures of Accuracy
High Accuracy
High Precision
Low Accuracy
High Precision
Low Accuracy
Low Precision
High Accuracy
Low Precision

## Slide 39: Measures of Accuracy
1D rms root mean square 68.3% 
2D error ellipse 39.4% E, N &
correlation
2drms twice distance root 95.4%  =E2+N2
mean square
3D error ellipsoid 19.9% X, Y, Z &
correlation






## Slide 40: Dilution of Precision (DOP)
  GDOP -Geometric Dilution of Precision GDOP = E2+ N2+ h2+ T2
  PDOP -Positional Dilution of Precision PDOP = E2+ N2+ h2
  HDOP -Horizontal Dilution of Precision HDOP = E2+ N2
  VDOP -Vertical Dilution of Precision VDOP = h2
Poor GDOP
Good GDOP

## Slide 41: Signal-to-Noise Ratio
The S/N of a signal is the ratio of received signal power, S, to the noise power, N, accompanying the signal. It is a unitless quantity and is typically expressed in decibels (dB). The noise may be caused by the receiver itself due to the random motion of electrons in its circuitry (thermal noise), by natural emissions such as ground and atmospheric radiation picked up by the antenna, or by interfering transmitters. The S/N is a measure of the quality of signals. In general, the higher the S/N the more accurate a GPS range measurement will be.
Usually, the higher the elevation angle of the received satellite, the higher the signal power (with the exception that when a satellite is near the zenith, the received power decreases slightly due to the shape of the satellite's transmitting antenna beam).
http://www.findarticles.com/p/articles/mi_m0BPW/is_10_13/ai_n9778491

## Slide 42: Single Point Positioning (SPP)

## Slide 43: Single Point Positioning
The Global Positioning System
Measurements of code-phase arrival times from at least four satellites that are used to estimate four quantities: Position in three dimensions (X,Y,Z) and GPS time (T)
X,Y,Z,T
,,h,T

## Slide 44: Pseudo-Ranges
(X,Y,Z)s : Cartesian coordinates of satellites
(X,Y,Z)r : Cartesian coordinates of receivers
dtr : receiver clock error
dts : satellite clock error
C : speed of light

## Slide 45
Ref: http://www.colorado.edu/geography/gcraft/notes/gps/gps_f.html

## Slide 46: Single Point Positioning

## Slide 47: Navigation with SPP

## Slide 48: Have a nice week !
Thank you ...