## Slide 1: GPS Technique
Assoc. Prof. Dr. Rahmi Nurhan ÇELİK
ITU Department of
Geodesy & Photogrammetry
Division of Geodesy
Tel: 0212-2853822
celikn@itu.edu.tr
http://atlas.cc.itu.edu.tr/~celikn

## Slide 2: Table of Contents
Space Techniques
What is GPS?
History of GPS.
How GPS works?
GPS Segments
  Space Segments
  Control Segments
  User segments
Positioning with GPS
  Measures of Accuracy
  Single Point Positioning
  Differential GPS
  Static GPS
    Static
    Rapid Static
  Kinematic GPS
  Real Time GPS

## Slide 3: Table of Contents
GPS Error Sources
GPS Observables
Coordinate Systems, Datum
Coordinate Transformations
GPS Project Management
GPS Data & Data Processing
GPS Receivers
GPS Applications
GPS in Turkey

## Slide 4: GPS Error Sources
GPS errors are a combination of noise, bias, blunders.
Ref: http://www.colorado.edu/geography/gcraft/notes/gps/gps_f.html

## Slide 5: GPS Error Sources
Noise errors are the combined effect of PRN code noise (around 1 meter) and noise within the receiver noise (around 1 meter).
Bias errors result from Selective Availability and other factors
  Selective Availability (SA)
    SA is the intentional degradation of the SPS signals by a time varying bias. SA is controlled by the DOD to limit accuracy for non-U. S. military and government users. The potential accuracy of the C/A code of around 30 meters is reduced to 100 meters (two standard deviations).
Ref: http://www.colorado.edu/geography/gcraft/notes/gps/gps_f.html

## Slide 6: GPS Error Sources
  Selective Availability (SA)
    The SA bias on each satellite signal is different, and so the resulting position solution is a function of the combined SA bias from each SV used in the navigation solution. Because SA is a changing bias with low frequency terms in excess of a few hours, position solutions or individual SV pseudo-ranges cannot be effectively averaged over periods shorter than a few hours. Differential corrections must be updated at a rate less than the correlation time of SA (and other bias errors).
Ref: http://www.colorado.edu/geography/gcraft/notes/gps/gps_f.html

## Slide 7: GPS Error Sources
19950 Km
50 Km
Troposfer
Iyonosfer
200 Km

## Slide 8: GPS Error Sources
  Other Bias Error sources;
    SV clock errors uncorrected by Control Segment can result in one meter errors.
    Ephemeris data errors: 1 meter
    Tropospheric delays: 1 meter. The troposphere is the lower part (ground level to from 8 to 13 km) of the atmosphere that experiences the changes in temperature, pressure, and humidity associated with weather changes. Complex models of tropospheric delay require estimates or measurements of these parameters.
Ref: http://www.colorado.edu/geography/gcraft/notes/gps/gps_f.html

## Slide 9: GPS Error Sources
  Other Bias Error sources;
    Unmodeled ionosphere delays: 10 meters. The ionosphere is the layer of the atmosphere from 50 to 500 km that consists of ionized air. The transmitted model can only remove about half of the possible 70 ns of delay leaving a ten meter un-modeled residual.
    Multipath: 0.5 meters. Multipath is caused by reflected signals from surfaces near the receiver that can either interfere with or be mistaken for the signal that follows the straight line path from the satellite. Multipath is difficult to detect and sometime hard to avoid.
Ref: http://www.colorado.edu/geography/gcraft/notes/gps/gps_f.html

## Slide 10: GPS Error Sources
Blunders can result in errors of hundred of kilometers.
      Control segment mistakes due to computer or human error can cause errors from one meter to hundreds of kilometers.
      User mistakes, including incorrect geodetic datum selection, can cause errors from 1 to hundreds of meters.
      Receiver errors from software or hardware failures can cause blunder errors of any size.
Noise and bias errors combine, resulting in typical ranging errors of around fifteen meters for each satellite used in the position solution.

## Slide 11: GPS Error Sources
Geometric Dilution of Precision (GDOP) and Visibility
  GPS ranging errors are magnified by the range vector differences between the receiver and the SVs. The volume of the shape described by the unit-vectors from the receiver to the SVs used in a position fix is inversely proportional to GDOP.
    Poor GDOP, a large value representing a small unit vector-volume, results when angles from receiver to the set of SVs used are similar.
    Good GDOP, a small value representing a large unit-vector-volume, results when angles from receiver to SVs are different.
Ref: http://www.colorado.edu/geography/gcraft/notes/gps/gps_f.html

## Slide 12: Good GDOP

## Slide 13: Poor GDOP

## Slide 14: GPS Error Sources
Geometric Dilution of Precision (GDOP) and Visibility
  GDOP is computed from the geometric relationships between the receiver position and the positions of the satellites the receiver is using for navigation. For planning purposes GDOP is often computed from Almanacs and an estimated position. Estimated GDOP does not take into account obstacles that block the line-of-sight from the position to the satellites. Estimated GDOP may not be realisable in the field.
  GDOP terms are usually computed using parameters from the navigation solution process.
Ref: http://www.colorado.edu/geography/gcraft/notes/gps/gps_f.html

## Slide 15
Ref: http://www.colorado.edu/geography/gcraft/notes/gps/gps_f.html

## Slide 16: GPS Error Sources
Geometric Dilution of Precision (GDOP) and Visibility
  In general, ranging errors from the SV signals are multiplied by the appropriate GDOP term to estimate the resulting position or time error. Various GDOP terms can be computed from the navigation covariance matrix. ECEF XYZ DOP (Earth Centred Earth Fixed XYZ DOP) terms can be rotated into a North-East Down (NED) system to produce local horizontal and vertical DOP terms.
  GDOP Components
    PDOP = Position Dilution of Precision (3-D), sometimes the Spherical DOP.
    HDOP = Horizontal Dilution of Precision (Latitude, Longitude).
    VDOP = Vertical Dilution of Precision (Height).
    TDOP = Time Dilution of Precision (Time).
Ref: http://www.colorado.edu/geography/gcraft/notes/gps/gps_f.html

## Slide 17: GPS Error Sources
Geometric Dilution of Precision (GDOP) and Visibility
  While each of these GDOP terms can be individually computed, they are formed from covariances and so are not independent of each other. A high TDOP (time dilution of precision), for example, will cause receiver clock errors which will eventually result in increased position errors.
Ref: http://www.colorado.edu/geography/gcraft/notes/gps/gps_f.html

## Slide 18
Ref: http://www.colorado.edu/geography/gcraft/notes/gps/gps_f.html

## Slide 19: Dilution of Precision (DOP)
  GDOP -Geometric Dilution of Precision GDOP = E2+ N2+ h2+ T2
  PDOP -Positional Dilution of Precision PDOP = E2+ N2+ h2
  HDOP -Horizontal Dilution of Precision HDOP = E2+ N2
  VDOP -Vertical Dilution of Precision VDOP = h2
  TDOP -Time Dilution of Precision TDOP = t2
Poor GDOP
Good GDOP

## Slide 20: Standard error model - L1 C/A (no SA)
One-sigma error, m
Error source Bias Random Total DGPS
------------------------------------------------------------
Ephemeris data 2.1 0.0 2.1 0.0
Satellite clock 2.0 0.7 2.1 0.0
Ionosphere 4.0 0.5 4.0 0.4
Troposphere 0.5 0.5 0.7 0.2
Multipath 1.0 1.0 1.4 1.4
Receiver measurement 0.5 0.2 0.5 0.5
------------------------------------------------------------
User equivalent range
error (UERE), rms* 5.1 1.4 5.3 1.6
Filtered UERE, rms 5.1 0.4 5.1 1.5
------------------------------------------------------------
Vertical one-sigma errors--VDOP= 2.5 12.8 3.9
Horizontal one-sigma errors--HDOP= 2.0 10.2 3.1
Ref: http://www.cnde.iastate.edu/staff/swormley/gps/check_accuracy.html

## Slide 21: Standard error model - L1 C/A (with SA)
One-sigma error, m
Error source Bias Random Total DGPS
------------------------------------------------------------
Ephemeris data 2.1 0.0 2.1 0.0
Satellite clock (dither) 20.0 0.7 20.0 0.0
Ionosphere 4.0 0.5 4.0 0.4
Troposphere 0.5 0.5 0.7 0.2
Multipath 1.0 1.0 1.4 1.4
Receiver measurement 0.5 0.2 0.5 0.5
------------------------------------------------------------
User equivalent range
error (UERE), rms* 20.5 1.4 20.6 1.6
Filtered UERE, rms 20.5 0.4 20.5 1.5
------------------------------------------------------------
Vertical one-sigma errors--VDOP= 2.5 51.4 3.9
Horizontal one-sigma errors--HDOP= 2.0 41.1 3.1
Ref: http://www.cnde.iastate.edu/staff/swormley/gps/check_accuracy.html

## Slide 22: Precise error model, dual-frequency, P(Y) code
One-sigma error, m
Error source Bias Random Total DGPS
------------------------------------------------------------
Ephemeris data 2.1 0.0 2.1 0.0
Satellite clock 2.0 0.7 2.1 0.0
Ionosphere 1.0 0.5 1.2 0.1
Troposphere 0.5 0.5 0.7 0.1
Multipath 1.0 1.0 1.4 1.4
Receiver measurement 0.5 0.2 0.5 0.5
-----------------------------------------------------------
User equivalent range
error (UERE), rms* 3.3 1.5 3.6 1.5
Filtered UERE, rms 3.3 0.4 3.3 1.4
-----------------------------------------------------------
Vertical one-sigma errors--VDOP= 2.5 8.3 3.7
Horizontal one-sigma errors--HDOP= 2.0 6.6 3.0
Ref: http://www.cnde.iastate.edu/staff/swormley/gps/check_accuracy.html

## Slide 23: Have a nice week !
Thank you ...