## Slide 1: GPS Technique
Assoc. Prof. Dr. Rahmi Nurhan ÇELİK
ITU Department of
Geodesy & Photogrammetry
Division of Geodesy
Tel: 0212-2853822
celikn@itu.edu.tr
http://atlas.cc.itu.edu.tr/~celikn

## Slide 2: Table of Contents
Space Techniques
What is GPS?
History of GPS.
How GPS works?
GPS Segments
  Space Segments
  Control Segments
  User segments
Positioning with GPS
  Measures of Accuracy
  Single Point Positioning
  Differential GPS
  Static GPS
    Static
    Rapid Static
  Kinematic GPS
  Real Time GPS

## Slide 3: Table of Contents
GPS Error Sources
GPS Observables
Coordinate Systems, Datum
Coordinate Transformations
GPS Project Management
GPS Data & Data Processing
GPS Receivers
GPS Applications
GPS in Turkey

## Slide 4: Relative Positioning with GPS

## Slide 5: GPS for Surveying
All GPS Surveying is carried out using differential techniques. That is to say a baseline is measured from a fixed point, (a reference station) to an unknown point (a rover station).
This is undertaken using one of two methods :
  Post Processing The raw GPS data from the satellites is recorded and processed in the office using software
  Real Time The processing of the data is carried out as you work, giving an instantaneous and accurate position

## Slide 6: Static & Rapid Static Survey

## Slide 7: Static Survey

## Slide 8: Static Survey
The classical method for long baselines.
The highest accuracy can be achieved by this technique
    Baseline rms: 5mm + 1ppm
  Classical GPS baseline measurement, where each line is observed for at least one hour.
  The observation time is proportional to the length of the baseline.
  Standard method for baselines over 20 Km

## Slide 9: Static Survey
General Applications
  Geodetic control survey over large areas
  National and continental networks
  Monitoring tectonic movement
  Monitoring Strong Motions
  Special Surveys for highest accuracy
  . . .

## Slide 10: Static Survey

## Slide 11: Rapid Static Survey

## Slide 12: Rapid Static Survey
Short observation time for baselines up to 20 km.
Baseline rms : 5-10 mm + 1 ppm
  General Applications
  Control Surveys,
  Control Network Densification
  Precise Traversing, Traversing, Local Networks.
  When high accuracy required for short baselines
Advantages of rapid static versus static survey
  Easy, quick, efficient, economic
  but only for short range survey

## Slide 13: Rapid Static Survey

## Slide 14: Rapid Static Survey Using 2 Receivers
Ref 1
4
5
6
7
3
2
1
1 Reference and 1 Rover
8
Rover
Rover
Rover
Rover
Rover
Rover
Rover
Rover
Reference

## Slide 15: Rapid Static Survey Using 2 Receivers
Ref 1
4
5
6
7
3
2
1
1 Reference and 1 Rover
2 Reference and 1 Rover
Ref2
Reference
Rover
Rover
Rover
Rover
Rover
Rover
Rover

## Slide 16: Rapid Static Survey Using 2 Receivers
Ref 1
4
5
6
7
3
2
1
1 Reference and 1 Rover
Rover
Reference
Rover
Reference
Reference
Rover
Rover
Reference
Ref2
6
7
Reference
Rover
7
1
Reference
Rover
2
1
Reference
Rover
Rover
Rover
1 Reference and 1 Rover (leap frog)
2 Reference and 1 Rover

## Slide 17: Kinematic Survey

## Slide 18: Stop & Go Survey

## Slide 19: Stop and Go Survey
Kinematic mode with static intervals
Baseline rms : 10 - 20 mm + 1 ppm
Stop Mode
  Before the survey begins, the rover is required to resolve the ambiguities.
  The ambiguities are resolved using one of three techniques
  Initialization on the fly
  Static initialization
  Initialization on a known point
Rover
Initialization
Ref. Station

## Slide 20: Stop and Go Survey
Rover
Initialized
Ref. Station
1
2
3
4
5
Go Mode
  Once enough data is collected to resolve the ambiguities, user can now move the receiver
  Lock must be maintained on a minimum of 4 satellites at all time
  Each point visited requires only 1 epochs of data
  If lock is lost, the system must re-initialize
Applications:
  Detail and engineering surveys in open areas

## Slide 21: Continuous Kinematic (KIS) Survey

## Slide 22: Continuous Kinematic
23 : 10 :22
23 : 10 :24
23 : 10 :26
23 : 10 :27
23 : 10 : 28
23 : 10 :30
23 : 10 :12
23 : 10 :14
23 : 10 :16
23 : 10 :18
23 : 10 : 20
23 : 10 :18
23 : 10 : 20
Baseline rms : 10 - 20 mm + 1 ppm
Stop Mode
  The rover must first initialize
Moving Mode
  Once enough data is collected to resolve the ambiguities, user can now move the receiver
  Lock must be maintained on a minimum of 4 satellites at all time
  Rover records data at a specific time interval
  If lock is lost, the system must re-initialize

## Slide 23: Kinematic on the Fly (KOF) Survey

## Slide 24: Kinematic On the Fly
23 : 10 :22
23 : 10 :24
23 : 10 :26
23 : 10 :27
23 : 10 : 28
23 : 10 :30
23 : 10 :12
23 : 10 :14
23 : 10 :16
23 : 10 :18
23 : 10 : 20
23 : 10 :18
23 : 10 : 20
Moving Mode
  This technique does not require a static initialization
  While moving, once the rover is continuously tracking a minimum of 5 satellites on the L1 & L2 for a period of time, the ambiguities can be resolved
  Travelling under an obstruction will cause a loss of lock
Baseline rms : 10 - 20 mm + 1 ppm

## Slide 25: Kinematic On the Fly
Moving Mode
Ambiguity resolution will re-establish once 5 satellites on L1 & L2 are acquired and tracking is consistent for a short period of time
  This technique allows positions to be determined up to the point that the minimum satellites were re-acquired
23 : 10 :55
23 : 10 :54
23 : 10 :53
23 : 10 :52
23 : 10 : 51
23 : 11 :00
23 : 10 :59
23 : 10 :58
23 : 10 :57
23 : 10 : 56
23 : 11 :02
23 : 11 : 01
23 : 10 :22
23 : 10 :24
23 : 10 :26
23 : 10 :27
23 : 10 : 28
23 : 10 :30
23 : 10 :12
23 : 10 :14
23 : 10 :16
23 : 10 :18
23 : 10 : 20
23 : 10 :18
23 : 10 : 20

## Slide 26: Real-Time Kinematic Survey

## Slide 27: Real Time Kinematic Survey
Real Time Code, Real Time Phase
No post processing required
Results are instantly available
Can operate in two modes
RT-Receiver Format
RT-Standard Format
B
A

## Slide 28: Real-Time Survey

## Slide 29: Real-Time Survey

## Slide 30: Baseline Accuracy and Observation Times
Baseline
Length
Number of
Satellites
GDOP
Observation
Time
Accuracy
20 - 50 Km
50 - 100 Km
> 100 Km
2 - 3 hr
min. 3 hr
min. 4 hr
5 mm + 1 ppm
5 mm + 1 ppm
5 mm + 1 ppm
Static :
Rapid Static :
Baseline
Length
Number of
Satellites
GDOP
Observation
Time
Accuracy
0 - 5 Km
5 - 10 Km
10 - 20 Km
5 - 10 min
10 - 15 min
10 - 30 min
5 - 10 mm + 1 ppm
5 - 10 mm + 1 ppm
5 - 10 mm + 1 ppm
4
4
4
5
5
5
4
4
4
6
6
6

## Slide 31: Recommended Recording Intervals
Operation
Type
Recording
Interval
Static
Rapid Static
Stop and Go
Kinematic
Kinematic On the Fly
10 sec
5 - 10 sec
1 - 5 sec
0.1 sec or more
0.1 sec or more

## Slide 32: DGPS Differential Global Positioning System

## Slide 33: What is DGPS?
Differential GPS (DGPS) is the regular Global Positioning System (GPS) with an additional correction (differential) signal added.
This correction signal improves the accuracy of the GPS and can be broadcast over any authorised communication channel.

## Slide 35: Pseudo-Ranges
(X,Y,Z)s : Cartesian coordinates of satellites
(X,Y,Z)r : Cartesian coordinates of receivers
dtr : receiver clock error
dts : satellite clock error
C : speed of light

## Slide 36: DGPS Pseudo-Range Corrections
rci : geometric range at reference station
roi : observed range at reference station
i : satellite number
m : number of reference station

## Slide 37: DGPS Error Sources User Equivalent Range Error
-----------------------------------------------------------------------------
Bias Souses SA-on SA-off DGPS
------------------------------ -------------------------------------------
Satellite clock offset 1-3 m 1-3 m 0
Ephemeris bias 2-7 m 2-7 m 0
Ionospheric delay 2-15 m 2-15 m 0~
Tropospheric delay 0.5-2 m 0.5-2 m 0~
Selective Availability 30 m 0 0
Receiver noise & multipath 1-3 m 1-3 m 1-4 m
------------------------------ -------------------------------------------
User Equivalent Range error 30-35 m 3-17m 1-4 m
------------------------------ -------------------------------------------
Positional error 90-115 m 9-51 3-12 m
-----------------------------------------------------------------------------

## Slide 38: Standard DGPS Corrections Radio Technical Commission for Maritime Services Special Committee No: 104 RTCM SC -104

## Slide 39: DGPS CORRECTION MESSAGE FORMAT
GENERAL MESSAGE 16 MESSAGE TYPES
INFORMATION
1- Differential corrections 2- Delta differential corrections
3- Station parameters 4- Surveying
5- Constellation health 6- Null Frame
7- Beacon health 8- Pseudolite health
9- High rate diff. Corr. 10- P-code diff. Corr.
11- C/A code L1, L2 diff. Corr. 12- Health message
13- To be decided 14- To be decided
15- To be decided 16- Special message

## Slide 40: RTCM Message
01 DGPS corrections 02 Delta DGPS corrections 03 Reference station parameters 04 Carrier surveying information 05 Constellation health 06 Null frame 07 Marine radio beacon almanacs 08 Pseudolite almanacs 09 High rate DGPS corrections 10 P code DGPS corrections 11 C/A code L1/L2 delta corrections 12 Pseudolite station parameters 13 Ground transmitter parameters 14 Surveying auxiliary message 15 Ionospheric/tropospheric message 16 Special message 17 Ephemeris almanac 18-59 Undefined 60-63 Differential Loran C messages

## Slide 41: Some Application of GPS
Marine, Aviation, Railway, Car Navigation
Vehicle Tracking
Fleet Management
GIS Data Collection
Precise Agriculture
.....

## Slide 42: DGPS Correction Service Providers

## Slide 43: Have a nice week !
Thank you ...