## Slide 1: GPS Technique
Assoc. Prof. Dr. Rahmi Nurhan ÇELİK
ITU Department of
Geodesy & Photogrammetry
Division of Geodesy
Tel: 0212-2853822
celikn@itu.edu.tr
http://atlas.cc.itu.edu.tr/~celikn

## Slide 2: Table of Contents
Space Techniques
What is GPS?
History of GPS.
How GPS works?
GPS Segments
  Space Segments
  Control Segments
  User segments
Positioning with GPS
  Measures of Accuracy
  Single Point Positioning
  Differential GPS
  Static GPS
    Static
    Rapid Static
  Kinematic GPS
  Real Time GPS

## Slide 3: Table of Contents
GPS Error Sources
GPS Observables
Coordinate Systems, Datum
Coordinate Transformations
GPS Project Management
GPS Data & Data Processing
GPS Receivers
GPS Applications
GPS in Turkey

## Slide 4: GPS Observables

## Slide 5: GPS Observables
L1 The carrier phase measurement on the L1 frequency
L2 The carrier phase measurement on the L2 frequency
C/A The pseudorange measurement on the L1 frequency
P1 The pseudorange measurement on the L1 frequency
P2 The pseudorange measurement on the L2 frequency
L1 frequency 1575.42 MHz.  = 19 cm
L2 frequency 1227.60 MHz.  = 24 cm
The Navigation Message also modulates the L1-C/A code signal. The Navigation Message is a 50 Hz signal consisting of data bits that describe the GPS satellite orbits, clock corrections, and other system parameters.

## Slide 6: GPS Satellite Signals
Fundamental Frequency 10.23 MHz
x 154
x 120
L1 1575.42 MHz
L2 1227.60 MHz
C/A Code 1.023 MHz
P-Code 10.23 MHz
P-Code 10.23 MHz
÷ 10
50 BPS
Satellite Message

## Slide 7: GPS Satellite Signals

## Slide 8: Range Determination from Code Observation
Pseudoranges (Code)
  Each satellite sends a unique signal which repeats itself approx.. every 1 msec
  Receiver compares self generated signal with received signal
  From the time difference (T) a range observation can be determined
  Receiver clock needs to be synchronized with the satellite clock
T
D = c (T)
Received Code
from Satellite
Generated
Code from
Receiver
Notes: Notes :

## Slide 9: Code Measurements

## Slide 10: C/A Code
The C/A code is a pseudo random (PN) binary code (states of 0 and 1) consisting of 1,023 elements, or chips, that repeats itself every millisecond.
The term pseudo random is used since the code is apparently random although it has been generated by means of a known process, hence the repeatability.
Due to the chipping rate (the rate at which each chip is modulated onto the carrier) of 1.023Mbps, the chip length corresponds to approximately 300m in length and due to the code length, the ambiguity is approximately 300km - ie the complete C/A code pattern repeats itself every 300km between the receiver and the satellite.
The C/A code can be thought of as a number of rulers extending from the satellite to the receiver. The length of each ruler is approximately 300km, and each graduation is 300m apart.
Ref: Quest

## Slide 11: C/A Code
The code is generated by means of a linear feedback register which is a hardware device representing a mathematical PN algorithm.
The sequences that are used are known as Gold codes which have particularly good autocorrelation and cross correlation properties. The cross correlation properties of the Gold codes are such that the correlation function between two different sequences is low - this is how GPS receivers distinguish between signals transmitted from different satellites.
Ref: Quest

## Slide 12: P Code
The P code, or precise code, is a long binary code that would repeat only every 38 weeks (Pratt, 1992).
Despite the code being shortened to a one week repeatability because each satellite transmits a different weekly section of the code, there is still no ambiguity between the satellite and receiver.
The P code can be thought of as a ruler extending from the satellite to the receiver. The length of the ruler is approximately one week multiplied by the speed of light, and each graduation is 30m apart.
Ref: Quest
Rapid access to the relevant part of the code for a particular satellite is carried out by means of a hand-over-word obtained from the broadcast data message.
The chipping rate is at 10.23 MHz resulting in a chip length of approximately 30 m.

## Slide 13: Range Determination from Phase Observation
Phase Observations
  Wavelength of the signal is 19 cm on L1 and 24 cm on L2
  Receiver compares self-generated phase with received phase
  Number of wavelengths is not known at the time the receiver is switched on (carrier phase ambiguity)
  As long as you track the satellite, the change in distance can be observed (the carrier phase ambiguity remains constant)
T
D = c TN
Received Phase
from Satellite
Generated
Phase from
Receiver
Notes: Notes :

## Slide 14
Phase Observables Equation
errors
t
t
N
t
c
f
t
A
j
j
A
j
A
j
A






)
(
)
(
)
(
)
(




: geometric range from station A to satellite k
: initial unknown integer number of cycles between k & A
: phase measured at station A for satellite k at time t
f : frequency of signal
c : speed of light
: Satellite clock error
Where,
k
A

k
A
N
k
A

k

A

: Receiver clock error
What Errors ?
Tropospheric refraction + ionospheric refraction+ multipathing effects
+ antenna phase centre offset & variation + noise & biases + etc.

## Slide 15: Single Differences
These are used to reduce satellite clock and orbit errors, and localised atmospheric errors.

## Slide 16
errors
t
t
N
t
c
f
t
A
k
k
A
k
A
k
A






)
(
)
(
)
(
)
(




Phase equation for station A and satellite k
errors
t
t
N
t
c
f
t
B
k
k
B
k
B
k
B






)
(
)
(
)
(
)
(




Phase equation for station B and satellite k
Single Difference Equation are obtained substituting eq.1 in eq.2
errors
t
N
t
c
f
t
AB
k
AB
k
AB
k
AB





)
(
)
(
)
(



(1)
(2)
Single Differences

## Slide 17: Double Differences
These are used to reduce satellite clock and orbit errors, localised atmospheric errors, and receiver clock errors.
This is usually the technique adopted by the final carrier phase GPS solution. Relative GPS also uses this approach.

## Slide 18
Single Difference for satellite k
c
errors
t
N
t
f
t
AB
k
AB
k
AB
k
AB





)
(
)
(
)
(



Single Difference for satellite j
errors
t
N
t
c
f
t
AB
j
AB
j
AB
j
AB





)
(
)
(
)
(



(1)
(2)
errors
N
t
c
f
t
kj
AB
kj
AB
kj
AB




)
(
)
(


Double Difference Equation substituting eq.1 in eq.2
Double Differences

## Slide 19
Generalised Mathematical Model for Double Differencing
 troposheric refraction ionospheric refraction multipathing effects
antenna phase centre offset & variationnoise






t
c
f
t
c
f
N
c
f
t
AB
j
B
j
A
k
B
k
A
AB
j
B
j
A
k
B
k
A
kj
AB
j
B
j
A
k
B
k
A
kj
AB















)
(
)
(
2
)
(
)
(
)
(





















Phase
difference
rate of change
of range
mean of receivers’
clock errors at A & B
difference between
two receiver
clock error
Total
integer ambiguity

## Slide 20: Triple Differences
This is the difference between two double differences from measurements recorded at subsequent epochs.
Assuming no cycle slips, or loss of lock has occurred, this eliminates the integer ambiguity. It is therefore used to detect for cycle slips and loss of lock.

## Slide 21: Initial Phase Ambiguity
Initial phase Ambiguity must be determined to use carrier phase data as distance measurements over time
Time (0)
Ambiguity
Initial
Phase Measurement
at Time (0)
Ambiguity
Time (1)
Measured
Phase Observable
at Time (1)

## Slide 22: What is Ephemeris?
Position at
time t1
X,Y,Z
Earth
Position at
time ?
X,Y,Z
Position at
time t3
X,Y,Z
Position at
time t2
X,Y,Z
Position at
time tn
X,Y,Z
Reporting its position
Reporting its position
Reporting its position
Reporting its position
Reporting its position

## Slide 23: Have a nice week !
Thank you ...