## Slide 1: GPS Technique
Assoc. Prof. Dr. Rahmi Nurhan ÇELİK
ITU Department of
Geodesy & Photogrammetry
Division of Geodesy
Tel: 0212-2853822
celikn@itu.edu.tr
http://atlas.cc.itu.edu.tr/~celikn

## Slide 2: GPS or GNSS !

## Slide 3: GNSS – what is it and does it make sense?

## Slide 4: GNSS Surveying and Future Satellite Signals What is GNSS?
  Global Navigation Satellite Systems, but generally speaking…
  The different independent satellite based navigation systems
    GPS – USA
      Primarily military system developed US DoD during the Cold War – part of Ronnie Reagan’s SDI (Strategic Defense Initiative)
    GLONASS (GLO) – Russia
      Developed in the 1980s to stay in “competition” with USA
    Galileo – European Union
      Efforts by the EU to become a competitor in the Space Industry and become independent from the USA

## Slide 5: GNSS Surveying and Future Satellite Signals Does GNSS make sense?
  Especially Galileo…
  Complete redundancy from other navigation systems is inevitable (but not yet possible (flight navigation…))
    Russia is not politically stable
    GPS alone is not sufficient
    Dependence on GPS is already today not to be underestimated
      Fewer fixed survey control points being maintained
      Computer networks time synchronized by GPS
    Who can guarantee the free availability of GPS signals in 2030?

## Slide 6: GNSS Surveying and Future Satellite Signals Does GNSS make sense?
  Especially Galileo… from a business/political point of view…
  Galileo is not expensive. To develop and build 30 satellites and construction of ground stations costs 3.2-3.4 billion Euro. Same cost as 150km of highway…
  Different studies estimate the annual market for related accessories and services as a consequence of Galileo to be 10 billion Euro with 100 000 jobs being created
  Considerable reduction in fatal accidents and traffic jams
    Cost of 40 000 fatal road traffic accidents per year for businesses is 1.5 - 2.5% of GDP of the EU.
    Cost of traffic jams approximately 2% of GDP.

## Slide 7: GNSS Surveying and Future Satellite Signals Does GNSS make sense?
  Especially Galileo… fact and fiction…
  GDP of the EU:
  Estimated Galileo Cost:
  EU Contribution:
  Promised business potential
  Promised additional jobs
  Estimated costs of traffic jams
  Promised savings of traffic jams
  GPS costs until 1995
  100‘000‘000‘000‘000
  3‘400‘000‘000
  1‘000‘000‘000
  10‘000‘000‘000
  100‘000
  2‘000‘000‘000‘000
  1‘000‘000‘000‘000
  $ 15‘000‘000‘000

## Slide 8: GNSS Surveying and Future Satellite Signals Why is GNSS interesting for surveyors?
  Current satellite availability…
  For example... in Hamburg
    Total GPS satellites: 28
    Average number visible above horizon: 7 (25%)
    Average number visible with only 50% horizon: 3 (13%)

## Slide 9: GNSS Surveying and Future Satellite Signals Why is GNSS interesting for surveyors?
  Future satellite availability…
  Generally with free horizons, GPS is sufficient
  But with obstructions (reality) every additional satellite is an advantage
  5 or more satellites required for fixing ambiguities

## Slide 10: GNSS – What comes? And when? And what benefits for the surveyor?

## Slide 11: GNSS Surveying and Future Satellite Signals GPS – What comes?
  L2C – “second civil frequency”
  New additional code on L2 (the second frequency)
  Stronger signal than L2P – allow positioning inside of buildings, only multi-meter accuracy
  Easier to track than encrypted P2 code
  Less precise than encrypted P2 code
  L2C phase is 90° opposite L2P phase
  L5 – “third civil frequency”
  New additional code on additional carrier frequency
  Allows additional linear combinations of frequencies to solve ambiguities
    Longer baselines with fixed ambiguities
    Quicker solving of ambiguities (instantaneous)
    More reliable in high iono conditions
  Tracking of L2C and L5 require new hardware

## Slide 12: GNSS Surveying and Future Satellite Signals GPS – What comes when?
  L2C – “second civil frequency”
  First GPS satellite (PRN17) with L2C launched in September 2005 and operational in December 2005
    Block IIR-M satellite – an additional 7 IIR-M satellites waiting to be launched
    GPS satellites only replaced when necessary – on average 2-3 satellites per year
  L5 – “third civil frequency”
  First GPS satellite (Block IIF satellite) with L5 is “in the queue”
    To be launched approximately in 2008
  So assuming 2.5 launches per year…
  2013 before a usable L5 constellation

## Slide 13: GNSS Surveying and Future Satellite Signals GPS – And what benefits for the surveyor?
  L2C – “second civil frequency”
  For the GPS manufacturer it is easier to track L2 (no benefit for surveyor)
  Marginally stronger signal
    But these weaker signals could deteriorate position solution since weak signals have in general higher noise – track L2C or L2P?
    0% benefit for a surveyor with L2C
  Difficult to mix reference with L2P and rover with L2C due to phase shift.
  L5 – “third civil frequency”
  Increase in redundancy of observations
    Slight accuracy improvements (appr. 5 %)
    Ambiguity resolution times reduced (instantaneous might be realstic)
    Ambiguity resolution possible over even longer baselines – competition with reference networks.
    0% benefit for a surveyor with L2C
    Noticeable improvements with FOC of L5

## Slide 14: GNSS Surveying and Future Satellite Signals GLONASS – What comes?
  L1 and L2 code and phase measurements
  Identical satellite signals but on different frequencies
    GPS has different signals on the same frequencies
  Inter-frequency biases between different satellites are difficult to remove
  Minimum of 2 GLONASS satellites must be observed in order to contribute to solving of GPS ambiguities
  L3 code and phase measurements
    Planned for next generation GLONASS satellites
    Same advantages as for GPS L5

## Slide 15: GNSS Surveying and Future Satellite Signals GLONASS – What comes when?
  1995
  Full constellation of 24 GLONASS satellites
  2001
  Reduced to 7 satellites
    On average less than 2 visible
  From 2000 onwards
  On average 3 satellites per year launched
  In 2006 17 usable satellites
  By 2008 full constellation should be available
  Useful constellation now available

## Slide 16: GNSS Surveying and Future Satellite Signals GLONASS – And what benefits for the surveyor?
  Additional satellites
  Generally speaking the more satellites the better

## Slide 17: GNSS Surveying and Future Satellite Signals GALILEO – What comes?
  “Open Service” - “Free” access to anyone
  2 (4) carrier frequencies
    E1 – code and phase
    E5a, E5b, Alt-BOC, code and phase
  Commercial Service” – “Restricted”
  1 frequency
    E6 – code and phase (needs hardware encryption in ASIC
  Signal structure for E1 and E5 band is similar to GPS, E1 signal is to large extent compatible with GPS
  Tracking Galileo signals requires in principle new receiver hardware
    A 3 frequency receiver

## Slide 18: GNSS Surveying and Future Satellite Signals GALILEO – What comes when?
  From the EU brochure 2002
  3 phases
    Development and validations of orbit (2002-2005)
      Agree mission targets
      Develop 3-4 satellites and ground component
      Prove the concept of the system
    Construction (2006-2007)
      Produce 27-28 satellites
      Install ground stations
    Commercial business (from 2008)

## Slide 19: GNSS Surveying and Future Satellite Signals GALILEO – What comes when?
  Reality
  28 December 2005
    First test satellite
  Contract for construction and operation of system is not yet signed
    Originally planned for 2001
  Delay of at least 3-4 years must be expected
  2011 before Galileo is operational

## Slide 20: GNSS Surveying and Future Satellite Signals GALILEO – And what benefits for the surveyor?
  Assumption
  Galileo as stand alone system will be at least as good as GPS
  Galileo and GPS combined on average 20% performance increase (availability, accuracy, range, speed)
  The Galileo ALT-BOC signal will have best multipath mitigation characteristics – 15-20 cm accuracy with differential code will be realistic
  Ambiguity resolution will be much easier – the reason why GLONASS does not give same benefit, is that wavelength are different for each satellite and the integer nature of double differences is gone.

## Slide 21: GNSS – Open questions...

## Slide 22: GNSS Surveying and Future Satellite Signals GNSS – Open questions…
  GPS L2C
  Track L2C or P2?
    L2C is stronger, but P2 is more precise
    Mixing (L2C from reference and P2 from rover) is always worse than identical tracking – and solving the phase ambiguity is difficult
    What advantage in tracking 1,2,3…12 L2C when the majority of the remaining satellites do not support L2C?
    How will the reference station operators decide?

## Slide 23: GNSS Surveying and Future Satellite Signals GNSS – Open questions…
  GPS L5
  3 frequency hardware is more expensive then 2 frequency
  What use is buying a 3 frequency receiver today when only after 2010 will more than 6 L5 satellites be available
  Would you buy a (more expensive) car now that can use a fuel additive to make your car more efficient, but the additive is only available in 2010?

## Slide 24: GNSS Surveying and Future Satellite Signals GNSS – Open questions…
  GLONASS
  3 frequency hardware is more expensive then 2 frequency
  A manufacturer independent data format will be difficult to realize for GLONASS
  How are GLONASS observations combined from the different sensor types – interfrequency biases need to be solved

## Slide 25: GNSS Surveying and Future Satellite Signals GNSS – Open questions…
  Galileo
  Assuming GPS and GLONASS are still around….
    From 2011, the following signals will be available
      GPS: L1, L2, L2C, L5
      GLONASS: L1, L2, L3
      Galileo: L1, E5a, E5b, ALT-BOC, (E6)
    Which signals and codes will reference network operators support?
    What RTK data format will be used?
    Which signals should the rover use (and to what extent)? Sometimes fewer is more

## Slide 26: GNSS Surveying and Future Satellite Signals Surveying with GNSS in 2016 …
2006
2016
28 GPS and 17 GLONASS SV
2 Frequencies (L1, L2)
26 observations on average per epoch without obstruction
12 observations with obstruction
RTK up to 30km
8“ typical initialization time
RTK accuracy ±15mm
24 GPS, 24 GLONASS SV, 30 Galileo
3 Frequencies (L1, L2, L5)
76 observations on average per epoch without obstruction
32 observations with obstruction
RTK up to 50km
1“ typical initialization time
RTK accuracy ±10mm

## Slide 27: Have a nice week !
Thank you ...