ITU    CIVIL ENGINEERING FACULTY

WATER SUPPLY AND ENVIRONMENTAL SANITATION

###### RECITATION 7 —

###### WATER NETWORK-HARDY-CROSS METHOD

1st Question:

hla = hlb = hlc		hl = f*V2*L / (D*2g) = 8*f*L*Q2 / (D5*2*g)

Hence; hl  1/D5

From these two relationship its easy to get	Lb / La = 32 and Lc / La = 243

2nd Question:

The red arrows and values on the figure refer to the initial guessed flow directions and discharges.

|  |  | PIPE No. | K | Q | KQn | KnQn-1 | Q |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Iteration 1 | Loop1 | 1 | 41 | 15 | 9225 | 1230 | 3.14 |
|  |  | 2 | 100 | 15 | -22500 | 3000 |  |
|  |  | 3 | 20 | 0 | 0 | 0 |  |
|  | Loop2 | 3 | 20 | 0 | 0 | 0 | 1.88 |
|  |  | 4 | 30 | 15 | 6750 | 900 |  |
|  |  | 5 | 50 | 15 | -11250 | 1500 |  |
| Iteration 2 | Loop1 | 1 | 41 | 18.14 | 13488.9 | 1487.3 | 0.10 |
|  |  | 2 | 100 | 11.86 | -14070.0 | 2372.3 | √ OK |
|  |  | 3 | 20 | 3.14 | 197.0 | 125.5 |  |
|  | Loop2 | 3 | 20 | 1.26 | -31.9 | 50.5 | 0.04 |
|  |  | 4 | 30 | 16.88 | 8543.0 | 1012.5 | √ OK |
|  |  | 5 | 50 | 13.13 | -8613.3 | 1312.5 |  |

3rd Question:

The red arrows and values on the figure refer to the initial guessed flow directions and discharges in “l/s”.

|  |  | PIPE No. | K | Q | KQn | KnQn-1 | Q |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Iteration 1 | Loop1 | 1 | 1 | 60 | 3600 | 120 | 1.82 |
|  |  | 2 | 3 | 40 | -4800 | 240 |  |
|  |  | 3 | 4 | 10 | 400 | 80 |  |
|  | Loop2 | 3 | 4 | 10 | -400 | 80 | -9.31 |
|  |  | 4 | 4 | 50 | 10000 | 400 |  |
|  |  | 5 | 2 | 25 | 1250 | 100 |  |
|  |  | 6 | 5 | 25 | -3125 | 250 |  |
| Iteration 2 | Loop1 | 1 | 1 | 61.82 | 3821.49 | 123.6 | -0.01 |
|  |  | 2 | 3 | 38.18 | -4373.55 | 229.1 | √ OK |
|  |  | 3 | 4 | 11.82 | 558.68 | 94.5 |  |
|  | Loop2 | 3 | 4 | 21.13 | -1785.13 | 169.0 | 0.62 |
|  |  | 4 | 4 | 40.69 | 6623.61 | 325.5 | √ OK |
|  |  | 5 | 2 | 15.69 | 492.53 | 62.8 |  |
|  |  | 6 | 5 | 34.31 | -5884.93 | 343.07229 |  |

# Text boxes

K=100
Q2=15 l/s

K=30

Q4=15 l/s

K=2
25

K=41

Q1=15l/s

K=3
40

K=5
25

K=4

50

K=1
     60

K=20
Q3= 0

K=50

Q4=15 l/s

a

b

c

2

Q

C

30lt/s

30lt/s

E

D

B

A

Q=25lt/s

Q=50lt/s

Q=25lt/s

Q=100lt/s

Q

K=4
    10

3

4

5

6

1