ITU    CIVIL ENGINEERING FACULTY

WATER SUPPLY AND ENVIRONMENTAL SANITATION

###### RECITATION 5 —

###### DESIGN OF RESERVOIRS

###### TO COMPANSATE CONSUMPTION FLUCTUATIONS

1st Question:

Total water consumption of a town during a day is given in the below table with referance to max. Qday as percentage. The water is supplied via a reservoir to which water is pumped from 08:00 to 18:00 (10 hours). Find the necessary reservoir volume to compensate the fluctuations excluding fire and maintenance tolerances (mean q day = 150 lt/ind./day, P = 100 000).

| Time (o’clock) | Percentage of max. Qday | Time (o’clock) | Percentage of max. Qday |
| --- | --- | --- | --- |
| 0-1 | 2 | 12-13 | 11 |
| 1-2 | 1 | 13-14 | 8.5 |
| 2-3 | 0.5 | 14-15 | 7 |
| 3-4 | 0.5 | 15-16 | 5 |
| 4-5 | 0.5 | 16-17 | 3 |
| 5-6 | 2.5 | 17-18 | 5 |
| 6-7 | 3 | 18-19 | 5 |
| 7-8 | 3 | 19-20 | 5 |
| 8-9 | 4 | 20-21 | 7 |
| 9-10 | 6 | 21-22 | 5 |
| 10-11 | 4 | 22-23 | 2 |
| 11-12 | 7.5 | 23-24 | 2 |