ISTANBUL TECHNICAL UNIVERSITY

GRADUATE SCHOOL OF SCIENCE ENGINEERING AND TECHNOLOGY

DEPARTMENT OF NAVAL ARCHITECTURE AND MARINE ENGINEERING

BOUNDARY ELEMENT METHODS IN SHIP HYDRODYNAMICS (GEM517E)

ONLINE COURSE

HOMEWORK 1

Due Date : November 26, 2020

1-) The following flow-field is considered for -(<x<( and -(<z<( (A and B are constants):

- Give an expression for A and B to define a physically meaningful flow.

- If the total flow velocity is equal to 1 m/s at x=1 m. and z=1 m., what is the relationship between A and B?

- Is the flow irrotational or rotational?

- Calculate and draw the particle trajectories.				     (25 points)

2-) It is known that the velocity potential of the flow-field you determined above can be expressed as:

- Determine C.

- Determine and draw the fluid velocity and acceleration velocity vectors at points A(x = z = 1 m.) and B(x = z = 2 m.). Draw also the flow streamlines through points A and B. What are the angles between the fluid velocity and the acceleration vectors at these two points?

- Determine the difference in pressure between points A and B (ρ=1000 kg/m3). Consider that A and B lie on the same horizontal plane.		     (25 points)

3-) A flow-field is given by the following velocity potential, ( (-( < x < ( and

-d < z < 0):

where d and L are known and k is a constant.

- Determine k in terms of the given constants.

- Determine the level z=constant on which the vertical velocity w is equal to 0 for all x. What does this level represent physically?			     (25 points)

4-) A 2-D vortex of strength ( and a 2-D discrete source of strength Q=( are 0.5 m. apart inside an unbounded horizontal fluid domain.

- Determine the location of point(s) in the vicinity of the two singularities where the pressure is equal to that at infinity.

- Do the same above in case of ground effect and for very high speed free surface effect? (Both singularities have a height from ground, h=1 m.)							      					     (25 points)

5-) Do the homeworks given in class.				               (100 points)