## Slide 1
Formation of the Dam Body
For Concrete Gravity dams:
Low-heat cements  to reduce shrinkage problem
Concrete is placed in “blocks”
“Keyways” are built between sections to make the dam act as a monolith
Upstream face
Upstream face
Downstream face
Downstream face
Keyways

## Slide 2
“Waterstops” are placed near upstream face to prevent leakage
Copper strip
Copper strip
Waterstops
“Inspection galleries” permit access to the interior of concrete
Dams and are needed for seepage determination, grouting operations and etc.

## Slide 3
Constructed in multi-layer formation
(Layers: impervious, filter and outer)
First place the materials in layers of 50 cm and then compact these materials.
For high dams, horizontal berms are constructed to enhance slope stability
Protect the upstream face of dam against wave action
(i.e., concrete or riprap)
For Earth-fill dams
Protect the downstream face against rainfall erosion
(i.e., planting grass or riprap)

## Slide 4
Silt
Silt clay
1 on 2.5
1 on 2
Sandy
gravel
Clay core
Silt
1 on 2.5
1 on 2.5
Silt
Transition zone
Pervious strata
Pervious foundation
Rock-fill toe
(a) Simple zoned embankment
(b) Earth dam with core extending to impervious foundation
Cross section of typical earth dams

## Slide 5
Silt
Silt clay
1 on 3.1
1 on 2
Sandy
gravel
1 on 3.8
Clay blanket
Concrete cutoff wall
Pervious material
(c) Earth dam on pervious material
Cross section of typical earth dams

## Slide 6
For Rock-fill dams:
Core and filter zones are similarly constructed as the earth dam
Due to heavy rocks on the sides, these dams
  have steeper slopes
  have less materials
  are economic
Construction period is shorter and easy to increase the crest elevation
Width of dam crest: There are two traffic lanes
Elevation of dam crest: There is no overtopping during design flood
Freeboard: See the table for recommendations

## Slide 7
Select Compacted Rock
1.3
1
1.3
1
Coarse
Dumped Rock
Reinforced Concrete Membrane
Cutoff wall
(a) Impermeable face
Dumped Rock
Rolled rock
Clay core
Dumped or
Rolled rock
Grout curtain
(b) Impermeable earth-core
Graded transition sections
(1.5m)
(0.2m)
1.4
1
1.4
1
Cross-section of typical Rock-fill dams
Rolled
Medium
Size
Rock

## Slide 8: GRAVITY DAMS
Recep YURTAL

## Slide 9
Resist the forces by their own weight
Concrete Gravity Dams

## Slide 10
Concrete Gravity Dams

## Slide 11
Concrete Gravity Dams

## Slide 12
Concrete Gravity Dams

## Slide 13
Why & Where we prefered?
  Sağlam ve geçirimsizliği sağlanabilecek yeterli kalınlıkta kaya temellerin uygun bir derinlikte bulunduğu orta genişlikteki vadilerde
  Yeterli miktarda ve istenen özellikte agrega malzemesinin bulunduğu, çimento naklinin ekonomik olduğu yerlerde
  Büyük taşkın debilerinin baraj gövdesi üzerinden mansaba aktarılması gereken durumlarda
  Baraj üzerinden bir ulaşım yolu geçirilmesi gereken durumlarda tercih edilir
  Savaş ve sabotaja karşı daha dayanıklı olması da ayrıca bir tercih nedeni olabilir.
Concrete Gravity Dams

## Slide 14
Types:
    Straight Gravity Dams
    Arch Gravity Dams
  Baraj ekseni, iki yamaç arasındaki en kısa bağlantıyı sağlayacak şekilde bir doğru ile birleştirilir.
  Temel kayasının yapısına, derzlere veya emniyet ihtiyacına bağlı olarak kavisli de yapılabilir.
Concrete Gravity Dams

## Slide 15
Design Criteria:
  En uygun kesit, etki eden en önemli dış kuvvet olan haznedeki hidrostatik su basıncı dağılımına uyum sağlayan, tabana doğru genişleyen üçgen kesit seçilir. Üçgenin tepesi genellikle haznedeki en yüksek su seviyesidir.
  Memba yüzeyi düşey veya %10 ‘u geçmeyecek şekilde eğimli yapılır.
  Baraj boş haldeyken çekme gerilmelerini önlemek, dolu haldeyken kayma ve devrilme emniyetini artırmak için yüksek barajlarda memba yüzeyi genellikle eğimli planlanır.
  Üçgenin tepe kısmında, duvar kalınlığını artırmak, yamaçlar arası ulaşımı sağlamak gibi nedenlerle dikdörtgen kesitli bir başlık bulunur.
Concrete Gravity Dams

## Slide 16
Concrete Gravity Dams
Design Criteria:

## Slide 17: Design Principles:
Ağırlık barajı hesaplarında üçgen profil gözönüne alınır.
Üçgen kesitin minimum boyutları, barajın kendi ağırlığı, hidrostatik su basıncı ve taban su basıncının etki ettiği normal yükleme durumunda çekme gerilmeleri meydana gelmeyecek şekilde belirlenir.
Bunun için:
b
H

Concrete Gravity Dams

## Slide 18
For the dam dimensions:
Check out the safety for
Overturning
Shear & sliding
Bearing capacity of foundation
No tensile stresses are allowed in the dam body
Concrete Gravity Dams

## Slide 19: Overturning Check
H
1/md
B

## Slide 20: Overturning Check
H
B

## Slide 21: Overturning Check
H
B

## Slide 22: Overturning Check
H
B

## Slide 23: Overturning Check
H
B

## Slide 24: Overturning Check
H
B

## Slide 25: Sliding Check
H
1/md
B

## Slide 26: Sliding Check
H
B

## Slide 27: Sliding Check
H
B

## Slide 28: Sliding Check
H
B

## Slide 29: Sliding Check
H
1/md
B

## Slide 30: Bearing Capacity Check
H
1/md

## Slide 31
3.5.1 FORCES ON GRAVITY DAMS
Free body diagram showing forces acting on a gravity dam

## Slide 32
The following loads should be considered:
A) WEIGHT (WC): Dead load and acts at the centroid of the section
B) HYDROSTATIC FORCES:
Water in the reservoir + tailwater causes Horizontal Hu Hd &
Vertical Fh1v Fh2v
C) UPLIFT FORCE (Fu): acts under the base as:

## Slide 33
D) FORCE OF SEDIMENT ACCUMULATION (Fs):
Determined by the lateral earth pressure expression
where
Fs : the lateral earth force per unit width,
γs : the submerged specific weight of soil,
hs : the depth of sediment accumulation relative to reservoir bottom elevation,
θ : the angle of repose.
   This force acts at hs /3 above the reservoir bottom.

## Slide 34
E) ICE LOADS (Fi): considered in cold climate
Ice force per unit width of dam (kN/m) can be determined
from the following table:
Thickness of ice sheet (cm) | Change in temperature (oC/hr) |  | 
 | 2.5 | 5 | 7.5
25 | 30 | 60 | 95
50 | 58 | 90 | 150
75 | 75 | 115 | 160
100 | 100 | 140 | 180

## Slide 35
F) EARTHQUAKE FORCE (Fd):
Acting horizontally and vertically at the center of gravity
k (earthquake coefficient): Ratio of earthquake acceleration to gravitational acceleration.

## Slide 36
G) DYNAMIC FORCE (Fw) :
In the reservoir, induced by earthquake as below
 Acts at a distance 0.412 h1 from the bottom
Fw : the force per unit width of dam
C : constant given by
θ’ : angle of upstream face of the dam from vertical (oC)
  For vertical upstream face  C = 0.7
'

## Slide 37
H) FORCES ON SPILLWAYS (∑F):
Determined by using momentum equation btw two successive sections:
ρ : the density of water
Q : the outflow rate over the spillway crest
ΔV: the change in velocity between sections 1 and 2 (v2-v1)
 Momentum correction coefficients can be assumed as unity.

## Slide 38
I) WAVE FORCES :
Considered when a long fetch exists
Usual loading
B &Temperature Stresses at normal conditions + C + A + E + D
Unusual loading
B & Temperature Stresses at min. at full upstream level + C + A +D
Severe loading
Forces in usual loading + earthquake forces
LOADING CONDITIONS:

## Slide 39
3.5.2 STABILITY CRITERIA
Dam must be safe against
(1) Overturning for all loading conditions
 resisting moments
 overturning moments
Safety factor:
F.SO  2,0 (usual loading)
F.SO  1,5 (unusual loading)

## Slide 40
(2) Sliding over any horizontal plane
f = friction coef. btw any two planes
Safety factor:
FSS  1,5 (usual loading )
FSS  1,0 (unusual or severe loading)
STABILITY CRITERIA

## Slide 41
STABILITY CRITERIA
(3) Shear and sliding together
A : Area of shear plane (m²)
τs : Allowable shear stress in concrete in contact with foundation
Safety factor:
FSss  5,0 (usual loading)
FSss  3,0 (unusual or severe loading)

## Slide 42
STABILITY CRITERIA
(4) Between foundation and dam contact stresses (σ) > 0
at all points
There are two cases for the base pressure:

## Slide 43: Base Pressure Check
CASE 1: e  B/6
B
ΣV
Ph
Pt
e
DAM BASE
Pt  s
Ph  s

## Slide 44: Base Pressure Check
Pt
B
e
DAM BASE
CASE 2: e > B/6
Pt  s
ΣV