## Slide 1
CHAPTER 1
INTRODUCTION
Ercan Kahya
Civil Eng. Dept., ITU
Water Resources, ITU - E. Kahya

## Slide 2
1.1 General
WR Engineer deals with
“Planning + design + construction & operation”
of WR systems to
CONTROL, UTILIZE & MANAGE
water efficiently.
Water Resources, ITU - E. Kahya

## Slide 3
* Systems Analysis 
to obtain optimum solution for the design & operation
of a WR system.
* Available fresh water in the earth < 1% of the total water
Recent significant concepts:
“SUSTAINABLE DEVELOPMENT”
Using & saving limited existing water resources for longer period with the desired quality
Water Resources, ITU - E. Kahya

## Slide 4
Water Resources, ITU - E. Kahya
“HYDROPOLITICS”
Sharing of international waters on the basis of water laws
The branch of WR Engineering is an interdisciplinary.

## Slide 5
Water Resources, ITU - E. Kahya
1.2 Characteristics of WR Projects
Uniqueness <no standardized design>
Uncertainty <hydrologic data!>
Socio-economic Aspect (GAP project)
Forecasting <based on the socio-economic growth required>
Economy of Scale
<The property is defined as: “Cost per unit capacity of WR systems decreases as the capacity needed increases.”>
Irreversibility
<No chance for cancellation or changing components of a completed dam>

## Slide 6
Water Resources, ITU - E. Kahya
1.3 WR Developments in Turkey
< Please, take a look at the text book! >

## Slide 7
CHAPTER 2
RESERVOIRS
Ercan Kahya
Civil Eng. Dept., ITU
Water Resources, ITU - E. Kahya

## Slide 8
Water Resources, ITU - E. Kahya
2.1 General
- Collection of water behind a dam or barrier for use during ??? flow period.
- ALSO for a water-supply, irrigation, flood mitigation or hydroelectric needs by drawing water directly from a stream
Fig. 1.1
During a specified time interval,
S (supply) < D (demand) :
 Need for “water storage”

## Slide 9
Water Resources, ITU - E. Kahya
Two categories of reservoirs:
1- Storage (conservation) [i.e., Atatürk dam]
2- Distribution (service) [for emergencies & fire fighting]
2.2 Physical Characteristics of Reservoirs
     Primary function is to store
     Most important characteristic: “storage capacity”

## Slide 10
Water Resources, ITU - E. Kahya
Elevation-Area-Volume Curves
- Given that location & dam height; to determine reservoir volume

## Slide 11
Water Resources, ITU - E. Kahya
“Area-elevation” curve:
by measuring the area enclosed within each contour in the reservoir site using a planimeter.
✪ Usually a 1/5000 scaled topographic map
“Elevation-storage” curve:
the integration of an area-elevation curve.
 The storage between any two elevations can be obtained by the product of average surface area at two elevations multiplied by the difference in elevation.
Elevation-Area-Volume Curves

## Slide 12
Water Resources, ITU - E. Kahya
Total reservoir storage components:
Normal pool level
Minimum pool level
Active storage
Dead storage
Flood control storage
Surcharge storage

## Slide 13
Water Resources, ITU - E. Kahya

## Slide 14
Water Resources, ITU - E. Kahya
General Guidelines for a reservoir site
Cost of the dam
Cost of real estate
Topographic conditions to store water
Possibility of deep reservoir
Avoiding from tributary areas < sediment-rich field >
Quality of stored water
Reliable hill-slopes < stable against landslides >

## Slide 15
Water Resources, ITU - E. Kahya
2.3 Reservoir Yield
Yield: the amount of water that reservoir can deliver in a prescribed interval of time.
 Depends on inflow and capacity
 Its relation with capacity is important in design
& operation of a storage reservoir.
Firm (safe) yield: the amount of water that can be supplied during a critical period.
 Period of lowest natural flow
 Never been determined by certainty…

## Slide 16
Water Resources, ITU - E. Kahya
Target yield: specified for a reservoir based on the estimated demands.
 The problem is to provide sufficient reservoir capacity with a risk of meeting the target.
Secondary yield: water available in excess of firm yield during high flow periods

## Slide 17
Water Resources, ITU - E. Kahya
  2.4 Selection of Capacity of a Storage Reservoir
Designing the capacity of a storage reservoir involves with determination of the critical period during
“Inflow < Demand”
In general, four methods to find out the capacity:
1- Flow (Discharge) run curve method
2- Mass curve
3- Sequent-peak algorithm
4- Operation study
5- Optimization analysis & stochastic models

## Slide 18
20
40
60
80
100
120
140
160
180
200
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Incoming, Demanded Volume (106 m³)
Time (month)
Incoming Volume
Flow Run Curve Method

## Slide 19
20
40
60
80
100
120
140
160
180
200
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Incoming Volume
Demanded Volume
Incoming, Demanded Volume (106 m³)
Time (month)
Flow Run Curve Method

## Slide 20
20
40
60
80
100
120
140
160
180
200
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Deficient
Volume
V1
V2
V3
V4
Incoming, Demanded Volume (106 m³)
Time (month)
Flow Run Curve Method

## Slide 21
20
40
60
80
100
120
140
160
180
200
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Deficient
Volume
Excessive
Volume
F1
F2
F3
Incoming, Demanded Volume (106 m³)
Time (month)
Flow Run Curve Method

## Slide 22
Excessive Volume: F
Deficient Volume: V
    F > V  Va = max V
    F = V  Va = max (F,V)
    F < V  Va = max F
Flow Run Curve Method

## Slide 23
Water Resources, ITU - E. Kahya
MASS CURVE ANALYSIS
Proposed by Ripple in 1883.
Graphical inspection of the entire record of historical (or synthetic) streamflow for a critical period.
Provides storage requirements by evaluating ∑(S-D)
Valid only when ∑D < ∑S during the period of record.
Works well when releases are constant.
Otherwise use of sequent-peak algorithm suggested.

## Slide 24
Water Resources, ITU - E. Kahya
Features of Mass Curve:
Cumulative plotting of net reservoir inflow.
Slope of mass curve gives value of inflow (S) at that time.
Slope of demand curve gives the demand rate (D) or yield.
The difference between the lines (a+b) tangent to the demand line (∑D) drawn at the highest and lowest points (A and B, respectively) of mass curve (∑S) gives the rate of withdrawal from reservoir during that critical period.

## Slide 25
Water Resources, ITU - E. Kahya
The maximum cumulative value between tangents is the required storage capacity (active storage).
 Note that 100% regulation (∑D = ∑S) is illustrated in Figure 2.4.

## Slide 26
S
S, D
(m³)
Time (month)
0
Incoming Flow Cumulative
Curve (IFCC)
Use of Mass Curve to Determine Reservoir capacity for a Known Yield:

## Slide 27
Time (month)
S
D
Annual Demand
1 year
S, D
(m³)
0
IFCC
Demand Cumulative Curve
Use of Mass Curve to Determine Reservoir capacity for a Known Yield:

## Slide 28
S
D
Annual Demand
1 year
S, D
(m³)
Zaman (ay)
0
IFCC
Use of Mass Curve to Determine Reservoir capacity for a Known Yield:

## Slide 29
S
D
Annual Demand
1 year
V1
V2
V3
S, D
(m³)
Time (month)
0
IFCC
Demand Cumulative Curve
Use of Mass Curve to Determine Reservoir capacity for a Known Yield:

## Slide 30
S
D
Annual Demand
1 year
V1
V2
V3
overflow
S, D
(m³)
Time (month)
0
IFCC
Demand Cumulative Curve
Use of Mass Curve to Determine Reservoir capacity for a Known Yield:

## Slide 31
S
D
Annual Demand
1 year
V1
V2
V3
overflow
S, D
(m³)
Time (month)
0
IFCC
Demand Cumulative Curve
Max. Reservoir
Capacity
Use of Mass Curve to Determine Reservoir capacity for a Known Yield:

## Slide 32
Water Resources, ITU - E. Kahya
Use of Mass Curve to Determine Reservoir capacity for a Known Yield:
Va = max {Vi}
SUMMARY: using the figure from your text book.

## Slide 33
Time (month)
S, D
(m³)
D
Use of Mass Curve to Find Possible Yield from a Fixed Size Reservoir

## Slide 34
V
V
V
D2
Time (month)
S, D
(m³)
D
Use of Mass Curve to Find Possible Yield from a Fixed Size Reservoir

## Slide 35
Time (month)
V
V
V
Slope = D1
D1
S, D
(m³)
D
Use of Mass Curve to Find Possible Yield from a Fixed Size Reservoir

## Slide 36
V
V
V
Slope = D1
Slope = D2
D2
D1
Time (month)
S, D
(m³)
D
Use of Mass Curve to Find Possible Yield from a Fixed Size Reservoir

## Slide 37
V
V
V
Slope = D1
Slope = D2
Slope= D3
D2
D1
D3
Time (month)
S, D
(m³)
D
Use of Mass Curve to Find Possible Yield from a Fixed Size Reservoir

## Slide 38
V
V
V
Slope = D1
Slope = D2
Slope = D3
D2
D1
D3
Time (month)
S, D
(m³)
D
Firm
Yield
Use of Mass Curve to Find Possible Yield from a Fixed Size Reservoir

## Slide 39
Water Resources, ITU - E. Kahya
Use of Mass Curve to Find Possible Yield from a Fixed Size Reservoir
D = min {Di}
SUMMARY: using the figure from your text book.

## Slide 40
Water Resources, ITU - E. Kahya
SEQUENT-PEAK ALGORITHM (SPA)
 SPA is a modification of the Mass Curve analysis for lengthy time series and particularly suited to computer coding.
The procedures involve the following steps:
1- Plot ∑(Inflow-Withdrawal): in symbolized fashion  ∑(S-D)

## Slide 41
t
(St – Dt)
(+)
(-)
SEQUENT-PEAK ALGORITHM (SPA)

## Slide 42
Water Resources, ITU - E. Kahya
2- Locate the initial peak and the next peak
(aka sequent peak),
3- Compute the storage required which is the difference between the initial peak and the lowest trough in the interval,
4- Repeat the process for all sequent peaks,
5- Determine the largest value of storages as
“STORAGE CAPACITY”.
SEQUENT-PEAK ALGORITHM (SPA)

## Slide 43
t
(St – Dt)
(+)
(-)
SEQUENT-PEAK ALGORITHM (SPA)

## Slide 44
t
(St – Dt)
(+)
(-)
V1
V2
V3
C = V2
SEQUENT-PEAK ALGORITHM (SPA)

## Slide 45
Water Resources, ITU - E. Kahya
Analytical solution to SPA is good for computer coding & use the equations below:
Vt = Dt – St + Vt-1 if positive
Vt = 0 otherwise
Vt : required storage capacity at the end of period t
Vt-1 : required storage capacity at the end of preceding period t
Dt : release during period t
St : inflow during period t
* Assign Vt=0 = 0
** Compute Vt successively for up to twice the record length
*** Va = max {Vt}
SEQUENT-PEAK ALGORITHM (SPA)

## Slide 46
106 m³
Monthly Demand Volume:
294 x % 85 = 250
Example:
Incoming monthly flow during the critical period (1973-1975) for Çatalan dam are given in the nearby table.
Find active volume of the reservoir for 85% regulation using SPA.
SEQUENT-PEAK ALGORITHM (SPA)

## Slide 47
106 m³
Analytical
Solution
Example Cont’d:
If positive
Vt = Dt – St + Vt-1
Otherwise
Vt = 0

## Slide 48
Graphical
Solution
Example Cont’d:

## Slide 49
Example Cont’d:

## Slide 50
Water Resources, ITU - E. Kahya
- defined as a simulated operation of the reservoir according to a presumed operation plan (or a set of rules)
- provides the adequacy of a reservoir
- based on monthly solution of hydrologic continuity equation
OPERATION STUDY

## Slide 51
Water Resources, ITU - E. Kahya
used to
a) Determine the required capacity,
b) Define the optimum rules for operation,
c) Select the installed capacity for powerhouses,
d) Make other decisions regarding to planning.
OPERATION STUDY

## Slide 52
Water Resources, ITU - E. Kahya
OPERATION STUDY
carried out
(1) only for an extremely low flow period & presents the required capacity to overcome the selected drought;
(2) for the entire period & presents the power production for each year.

## Slide 53
Water Resources, ITU - E. Kahya
Reliability of Reservoir Yield
See the text book & class discussion for the details
OPTIMIZATION ANALYSIS & STOCHASTIC MODELS

## Slide 54
Water Resources, ITU - E. Kahya
2.8 Reservoir Sedimentation
Sediments  eventually fill all reservoirs
determine the useful life of reservoirs
important factor in planning
■ River carry some suspended sediment and move
bed load (larger solids along the bed).
■ Large suspended particles + bed loads  deposited at the head of the reservoir & form delta.
■ Small particles  suspend in the reservoir or flow over the dam.

## Slide 55
Water Resources, ITU - E. Kahya

## Slide 56
Water Resources, ITU - E. Kahya
■ Bed load ≈ 5 to 25 % of the suspended load in the plain rivers
≈ 50 % of the suspended load in the mountainous rivers
☻ Unfortunately, the total rate of sediment transport in Turkey > 18 times that in the whole Europe
(500x106 tons/year)

## Slide 57
Water Resources, ITU - E. Kahya
“RESERVOIR SEDIMENTATION RATE”
▬ based on survey of existing reservoirs, containing
* Specific weight of the settled sediments
* % of entering sediment which is deposited
“TRAP EFFICIENCY”:
% of inflowing sediment retained in the reservoir
▬ function of the ratio of reservoir capacity to total inflow.

## Slide 58
Water Resources, ITU - E. Kahya

## Slide 59
Water Resources, ITU - E. Kahya
► “Prediction of sediment accumulation”
-- Difficult due to high range of variability in sediment discharge
► SOLUTION: “Continuous hydrologic simulation models”
-- used for prediction purposes
< But, at least, 2-3 years daily data are needed for calibration of the model. >
IMPORTANT NOTES:

## Slide 60
Water Resources, ITU - E. Kahya
IMPORTANT NOTES:
► “To control amount of entering sediment”:
(a) Upstream sedimentation basins,
(b) Vegetative screens,
(c) Soil conservation methods (i.e., terraces),
(d) Implementing sluice gates at various levels.
(e) Dredging of settled materials, but not economical!